VIZOP: FAULT TREE VIEWPORT SPEC: ACTION ITEMS

Level: 3
Revision: 0.1
Date: 12 Nov 2018

Peter Clarke

OVERVIEW
This document describes one of the Viewports provided in the Fault Tree PHA model: the Action items Viewport. It shows the complete list of action items or parking lot items in the fault tree in a display panel.

This Viewport should be standardised, where practicable, to match action items lists from other PHA models (e.g. HAZOP).

DETAILS OF VIEWPORT APPEARANCE AND BEHAVIOUR

Standard zoom and pan controls are available; see Control Frame spec for details.
Multiple instances of this Viewport are allowed.

Display overview
The overall display area is divided into 2 stacked areas: header and action items list.
The name of action items and parking lot items can be changed as a global project setting (e.g. changed to “Recommendations”). The appropriate name should be reflected in the display. Horizontal and vertical scrollbars may be required.

The Viewport will show either action items, or parking lot items. The user can invoke separate instances of this Viewport to view both kinds of associated text. It's not possible to change to the other kind within a given Viewport instance.

Header area
The header area contains overview information, including:
- Heading: “Action items” or “Parking lot items” (adjusted according to the open to show either or both, see below)
- Zoom tool
Below this are options relating to the whole grid:
- Text filter
- Filter to show only action items in the a specific FT, in all FTs in the project (if >1 exist), or in the whole project. [future]
- Tasks choice + “Go” button. The choice contains the following actions:
  - Delete all unused actions (i.e. any action items that are not attached to any objects in the project). Undoable. This menu item is shown only if any such unused actions exist. [future]
  - Convert parking lot items to action items. Affects only displayed parking lot items, taking search and filter into account. Undoable. This menu item is shown only if there are any parking lot items on display. [future]
  - Export. Does the same as the PHA model “export action items list” command, see separate specification.
  - Add to current scope. Adds selected associated text(s) to the active PHA element, then displays the Viewport containing the active PHA element (if not already visible in a display device).

The header area should be always visible. It should zoom, but should not pan along with the action items list area.

Action items list area
All action items in the FT are listed in a grid.

Grid properties:
- Column size and order is stored in the Viewport object, and should be restored when the Viewport is reopened after closing.
- Columns can be resized [future]
- Columns can be reordered [future]
- Rows can be resized. Row height should be stored as an attrib of the action item object. [future]
- Rows can be reordered. Reordering rows results in reordering (hence, renumbering) of the action items. [future]

Columns displayed:
- Action item number. If the action item is used in different contexts within the project (e.g. in HAZOP and in FT), the numbering is taken from whichever context is marked as the 'primary context' (which is an attribute of the action item instance).
- Text
- Responsibility
- Target completion date
- Places used (hyperlinks to all places in the entire project where this action item is used. When short left clicked, the display device changes to show a Viewport (e.g. full tree for FT) showing the item hosting the action item, with action items visible. If such a Viewport is already existing and not currently displayed, it is displayed. Otherwise, a new Viewport is created for this purpose. On long left click, a “preview display” is shown – same as short left click, but not editable, and reverts to the action item list when the mouse button is released)
- Whether it's an action item or parking lot item
- 'Tasks' button (spanner symbol?); when left clicked, it brings up a context menu offering the following commands:
  - Delete action item (undoable)
  - Duplicate (adds a copy of the action item immediately below the current item, without linking) (undoable)
  - Duplicate and link (undoable)