VIZOP: FAULT TREE PHA MODEL SPEC

Level: 2
Revision: 0.1
Date: 7 Nov 2018

Peter Clarke

OVERVIEW
This PHA model executes Fault Tree Analysis. It allows the user to construct a Fault Tree (FT), and calculates the frequency and/or probability of each event in the tree, given suitable input data. Eventually, the FTA will be consistent with IEC 61025, although compliance is not a top priority.

The FT can contain initiating events, logic gates (eg OR/AND), connecting lines, intermediate events, IPLs, conditional modifiers, connectors to/from other FTs, and outcomes.

Data for objects in the FT, such as causes and IPLs, can be pulled in from other parts of the project. For example, a HAZOP cause can be designated as an initiating event in a Fault Tree, without creating a new object (the FT object can derive its attributes from the associated HAZOP object. This is probably simpler than trying to make them actually be the same object).

The FT can be calculated for one or more “Risk Receptors” (RRs), such as Personnel injury or Environmental impact. RRs should be defined at project level.

Input values (frequency, severity) for an object in the FT can be linked to values from another object, or to a constant. Values can be numerical or selected from a list of categories. Overrides are available. Values can vary from one RR to another. This is all handled through the behaviour of standard NumValueItem objects.

Comment fields and action item hooks, with numbering, are available throughout.

OBJECT DEFINITIONS

Initiating events (causes)
These are instances of FTBaseEventItem. They can be in collapse groups. They have outputs only, no inputs. Their value is a frequency or probability. If the FT is in High demand mode or Continuous mode, exactly 1 initiating event needs to be designated as the “SIF failure event”, and its value will then be calculated automatically.

Independent protection layers (IPLs), Enabling conditions and Conditional modifiers
These are instances of IPLItem and CondModifierItem respectively.
IPLs (etc) are associated with one or more initiating events or intermediate events. The association is the same for all risk receptors, but the value (a probability, which can be displayed as probability of failure on demand (PFD) or risk reduction factor (RRF)) can vary per risk receptor. If an IPL (etc) gets disassociated from all events, it gets automatically deleted. (Future: Keep it in a “spare IPL” library?) They have outputs only, no inputs. They can be in collapse groups.

Intermediate events
These are instances of FTInterEventItem. They have an input from upstream (only 1) and ≥0 (optional) downstream output connection(s) to other objects. Their value, a frequency or probability, is calculated automatically according to their connectivity in the Fault Tree. They can have IPLs and conditional modifiers associated with them, and can be in collapse groups.

Outcomes
These are instances of FTOutcomeItem. They are attached to 0 or 1 upstream input object, which can be an initiating event, intermediate event, a logic gate output, or a connector-in. They have no outputs. (If the user desires to output the value to another FT, he needs to create a Connector-out, fed from the same source as the Outcome.) Their value, a frequency or probability, is calculated automatically according to their connectivity in the Fault Tree. For each Fault Tree, one outcome can optionally be designated as the “result”, and its value is displayed in the header.

Connector-in and -out
These are instances of FTConnectorItem. They are connected to 0 or 1 up/downstream item (upstream for connector-out, downstream for connector-in). Connectors-out have a text descriptor, which is a label shown inside. Connectors-in don't have their own descriptor, but show the descriptor of the 0 or 1 connector-out that they are associated with. Association must be with connectors on a different FT (i.e. association between an -in and an -out on the same FT is not allowed). Associations that create circular relationships are not allowed (e.g. connect FT #1 to FT #2, and connect FT #2 to FT #1). One -out can be associated with any number of -in’s, but each -in must be on a different FT (i.e. not allowed to connect to the same FT twice). All these rules are designed to ensure the FT calculation gives a valid result.

Logic gates
These are instances of [enter class name]. They are connected to ≥0 upstream items and ≥0 downstream items. Their connections are not allowed to create circular relationships. Their output value (frequency or probability) is calculated automatically from the inputs. The logic function is selectable from a list of functions such as AND, OR, and Mutually Exclusive OR.

Collapse groups
These are not actually FT objects, but groups of objects. They allow the user to collapse the group of objects into a single box in a Viewport or a Report, to allow the FT to be depicted more compactly on the screen or in the report. Nested collapse groups are allowed. A collapse group must contain ≥1 initiating event (or a collapse group containing ≥1 initating event, at any level of nesting), and optionally can contain any other FT objects, provided the following rules are met:
- For all objects in the collapse group, the upstream objects to which they are directly connected must all be in the same collapse group (or in a nested collapse group)
- All objects in the collapse group must be displayed contiguously, i.e. not allowed to “jump over” objects in a column.

DATA HIERARCHY
Most of the data for the FT is an attribute of a object within a Fault Tree class instance. The Fault Tree class is a subclass of PHAModel objects, and therefore is an attribute of a Project.

The objects in the FT are notionally arranged in columns, as if the FT were drawn from left to right (although there is no intrinsic reason why it has to be depicted this way).

The first column contains ≥0 of the following:
- initiating events
- Connectors-in
- Enabling conditions
- IPLs

The second column (and all subsequent even-numbered columns) contain ≥0 of the following:
logic gates

Subsequent odd-numbered columns contain ≥0 of the following:
initiating events
- intermediate events
- Connectors-in
- Connectors-out
- Enabling conditions
- IPLs
- Conditional modifiers
- Final events

Objects are logically connected from one column to the next. For example, an initiating event and some IPLs may be connected to the inputs of a logic gate. Connections between objects in the same column, in non-adjacent columns, or connections to themselves, are not allowed. Also, circular connections are not allowed (e.g. object #1 → objects #2 and #3 → object #4). If an illegal connection is found when an FT is opened from a project file, the illegal connection should be deleted and a warning issued in VizopTalks.

Attributes belonging directly to the FT instance

Attribute	Meaning	Notes
Columns	list of column instances
Severity	severity value of the outcome	NumValueItem instance with different values for each RR
CollapseGroups	list of collapse group instances
TolerableFreq	The tolerable frequency of the outcome of the FT	Tolerable frequency can be defined in one of the following ways: / A category selected from a list. The categories should be defined in a risk matrix at project level. Each category has an associated tolerable frequency value. / A frequency value (directly supplied by the user, not looked up from a risk matrix)

Attributes belonging to objects in FT columns
e.g. Initiating events, logic gates, IPLs

Attribute	Meaning	Notes
Output value	Frequency or probability value per RR	For initiating events, this is provided by the user or linked from another object in the project. For all other FT objects, this is automatically calculated based on the object's connectivity in the FT.
Comments	User supplied comments on various attributes	Following standard comments structure for all PHA objects. Comments can be attached to: description, value.
Actions	User supplied action items for follow-up	Following standard action item structure for all PHA objects.

Notes
Objects have no CollapseGroup attribute to indicate their membership of a collapse group. Membership shall be inferred by looking up in the collapse group instances.

Attributes belonging to collapse group instances

Attribute	Meaning	Notes
Members	list of all FT objects and other collapse groups belonging directly to this collapse group	Shall never be an empty list
CollapsedInViewport	dict with keys = instances of Viewports existing in this FT, values = boolean (whether the collapse group is collapsed in the Viewport)	All Viewports listed as keys in the dict shall exist. / Instances of Viewports (rather than Viewport classes) are used as keys because multiple Viewports of the same class could exist, with different settings for each Collapse group.
CollapsedInReport	dict with keys = classes of Reports available in FT PHAModel, values = boolean (whether the collapse group is collapsed in the class of report)

CALCULATIONS
All calculations are done in logic gates. As calculations are safety-critical, they should be segregated into validatable code.

The calculation algorithm of each class of logic gate is listed below. Calculations are implemented in method GetMyValue() of class FTGateInCore. Input validity checks are in method GetMyStatus() of this class.

Logic gate class	Brief description	Permissible inputs	Algorithm
OR	Multiple events can lead to the outcome. Events are not mutually exclusive.	All frequencies, or all probabilities	All frequencies: output = sum of inputs. TODO: fix the double counting this entails. / All probabilities: output = 1 – product(1 – inputN) for inputs input1..inputN
MutExcOR	Multiple events can lead to the outcome. Events are mutually exclusive.	All frequencies, or all probabilities	All frequencies: output = sum of inputs / All probabilities: output = sum(input1..inputN) for inputs input1..inputN, forced to ≤1
AND	All inputs must be true simultaneously to lead to the outcome. Input events are independent.	≤1 frequency, the remainder probabilities	product(input1..inputN) for inputs input1..inputN
NOR	All inputs must be false simultaneously to lead to the outcome. Input events are not mutually exclusive.	All probabilities	product(1 – inputN) for inputs input1..inputN
NAND	≥1 inputs must be false simultaneously to lead to the outcome. Input events are independent.	All probabilities	1 – product(1 – inputN) for inputs input1..inputN
2ooN	≥2 inputs must be true simultaneously to lead to the outcome. Input events are independent and not mutually exclusive.	All probabilities	Sum of probabilities of all combinations of inputs for which ≥2 inputs are true. The probability of each combination is calculated as product(inputN).
3ooN	≥3 inputs must be true simultaneously to lead to the outcome. Input events are independent and not mutually exclusive.	All probabilities	Sum of probabilities of all combinations of inputs for which ≥3 inputs are true. The probability of each combination is calculated as product(inputN).

Units for AutoNumValueItem instances
When an auto value is created for a logic gate, its unit is initially set to undefined. When the first input is connected to the element, the element's unit is set to the current unit of the input. The unit can subsequently be updated manually by the user.

When an auto value is created for an initiating event that is set as the SIF failure event, its unit should be dynamically linked to the unit of the tolerable frequency. (This is currently a TODO in SetAsSIFFailureEvent().)

VIEWPORTS
The FT can be depicted and/or edited through the following Viewports. Each Viewport is described in a separate spec.

Name of Viewport	Function	Notes
Full tree display	View all details of the full tree structure, including data, comments and action items	Fully editable. Can show Collapse groups expanded or collapsed.
Action items	Show table of action items	Some data editable.
Full tree report	Export an image of the full tree structure	See spec 392

REPORTS
The FT can be depicted through the following reports. Each report is described in a separate spec.

Name of report	Function	Notes
Full FT	Produce graphical image showing various levels of detail (up to and including all data and comments), suitable for export in appropriate graphical format (e.g. JPEG, TIFF)	Parameters relating to format are editable (e.g. level of detail, image size, split across how many pages). Can show Collapse groups expanded or collapsed.
Action items	Produce table of action items as Excel spreadsheet	Some data editable. Parameters relating to format are editable (e.g. level of detail). Viewable in a display device

VALUE CHECKS
Value checks can be performed on user-supplied values in the Fault Tree. Checks are initiated by the “run checks” command in a menu (TBC; see Control Frame spec for details). Checks are applied to user-defined, copied, linked or constant values.

Check number	Check	Notes
FT1	Value ≥ 0.0	Applies to all input frequencies and probabilities in initiating events and connectors-in
FT2	Value ≤ 1/day	Applies to input frequencies in initiating events and connectors-in
FT3	Value ≤ 1.0	Applies to input probabilities in initiating events and connectors-in

(incomplete)