VIZOP SPECIFICATION
PERSISTENCE

Level: 3
Version: 0.1 (under initial construction)

INTRODUCTION
This document defines all the data that needs to be stored by Vizop for persistence, that is, to allow Vizop to “remember” as needed. For example, when the user requests to open a project file, Vizop can remember the folder last used and offer it as a default.

This does not refer to project data, such as the detailed information in a PHA study. See “Format of input and output files”.

WHERE PERSISTENT DATA IS STORED
Persistent data is divided into several repositories as follows:

- Global data: data that is independent of the user and project. For example, license key.
- User data: data that may vary from one user to another. For example, most recent project opened.
- Internal data: data needed to be available to all code modules, such as license status, but not necessarily shared between Vizop instances.

GLOBAL DATA
This is stored in a platform-dependent location:
Platform	Folder	File name
Windows
MacOS
Linux

The stored data is as follows:

Attrib name	Meaning	Legal values	Default value
LicenseKey	The most recent license key entered by the user that successfully set the licensed status to “Licensed”	String of A~Z and 0~9, length ≥1	Empty string

Default values are used if the file cannot be read, or the read value is not one of the legal values.

The file is written on program exit. If the file cannot be written (e.g. read-only access to the folder), a text warning is provided in the stdout. There is no warning in the UI.

USER DATA
This is stored in a platform-dependent location:
Platform	Folder	File name
Windows
MacOS
Linux

The stored data is as follows:

Attrib name	Meaning	Legal values	Default value
PrimaryMonitor	The number of the monitor that the Welcome Screen or Control Frame was on, at last program exit	Integer ≥1	1
UnitOfLength	Default unit of length (for screen/export measurements)	string: cm, mm, in, '' (double quote meaning inch)	cm
To be added: folders last used for storing and opening project files

Default values are used if the file cannot be read, or the read value is not one of the legal values.

The file is written on program exit. If the file cannot be written (e.g. read-only access to the folder), a text warning is provided in the stdout. There is no warning in the UI.

INTERNAL DATA

The stored data is as follows:

Attrib name	Meaning	Legal values	Guaranteed to exist?
LicenseKey	The currently valid license key	See “Licensing” spec	Yes, if license is valid (as indicated by LicenseStatus)
LicenseStatus	Whether the user's license is valid	See “Licensing” spec	Yes

The “guaranteed to exist” field indicates whether procedures needing to read an attribute can assume it will exist, without the need for error trapping in case it doesn't exist.