VIZOP SPECIFICATION
 ALARM RATIONALIZATION - OVERVIEW

Level: 3
Version: 0.1 (under initial construction)

INTRODUCTION
This document defines the Alarm Rationalization (AR) PHA model.

PURPOSE
AR allows the user to work with alarms presented to the operator through the Human-Machine Interface (HMI) of the process control system.
The overall purpose is:
- Determine the purpose of each alarm in the system
- Define the minimum set of alarms required for safe operation
- Define core parameters of each alarm, such as the set point, process variable (PV) measured, instrument tag and whether it is high or low.
- Define operator response parameters such as the likely cause of the alarm, consequence of no response, priority level, and operator guidance text
- Define tuning parameters such as delay times
- Define alarm suppression parameters such as first-out groups.
The alarm list may contain many thousands of alarms, so it is important for the functions to work efficiently and allow the user to apply a single editing actions to multiple alarms.

MAIN FUNCTIONS
The key functions of the AR PHA model are:
- Import alarm data from spreadsheet
- Display and filter alarms in an alarm list Viewport
- Edit alarm parameters in various Viewports. Several different Viewports are provided for various groups of alarm parameters.
- Produce alarm statistical reports (e.g. priority distribution) as exports (later, on screen as well)
- Export the completed alarm list

IMPORT FUNCTION
Alarm data can be imported from Excel files only. (Later, we may add the capability to import from other file formats such as CSV, and from other Vizop project files.)
The import function is invoked from the Import alarm from Excel command in the File menu. This command is available only when an alarm list Viewport is visible in the main control frame. It is available only for fully licensed instances of Vizop.
When invoked, a new “import alarms” Viewport is created and displayed. This provides widgets to:
- Select the file name to import
- Select options for importing (e.g. whether to overwrite existing alarms)
- Specify which worksheet of the file to import (if it has >1 worksheet)
- Preview the first few rows of the file
- Specify how many header rows of the file to skip
- Inform the user how many alarms are found in the worksheet
- Select which columns to import, and which attributes are supplied in each column
- Go and cancel buttons

After the import is complete, the Viewport will be destroyed and the display device will show the alarm list (creating a new alarm list Viewport if none exists in the project). Attribute values entered by the user (e.g. column definitions) will be stored as attributes of the AR PHA model, and restored when the user next invokes the import command.

If the user clicks the Cancel button, the import Viewport will be destroyed, and the display device will show the Viewport that was visible when the import command was invoked.

LAYOUT OF THE IMPORT VIEWPORT

IMPORT ALARMS FROM FILE <static header>
Filename: <static>	PathName <expando>	SelectFilename <button>
Status <static>
Worksheet <static>	WorksheetChoice <choice>	Header rows:<static>	HeaderRowCount <spin>
OverwriteExistingAlarms <checkbox>
MultiLevel <checkbox>			Worksheets <static>	WorksheetCount <static>
Import priorities as override <checkbox>			Unique alarms <static>	UniqueAlarmCount <static>
Alarm tag style: <static>	ExampleInstrumentTag <static>	ExampleAlarmTag <text>	Duplicates <static>	DuplicateAlarmCount <static>
<gap>
LeftButton <button>	Col1Number <static>	Col2Number <static>	Col3Number <static>	RightButton <button>
	Col1Attrib <choice>	Col2Attrib <choice>	Col3Attrib <choice>
	First row preview <static>
	First row after header rows preview <static>
	Second row after header rows preview <static>
<gap>
	CancelButton <button>	GoButton <button>

Functions of widgets
PathName <expando>	Shows the full path of the selected filename. Prefilled with the last filename selected for alarm import in this project (whether or not it was actually imported), if any, else blank. Editable.
SelectFilename <button>	Open standard File Open dialogue. Default folder and file is the current contents of PathName, if any, else the last folder containing a file selected for alarm import in this project (whether or not it was actually imported), if any, else user home folder. File type is .xlsx by default. Only one file can be selected. If user provides a filename and clicks Open, the filename is populated into PathName. If the user clicks Cancel, the File Open dialogue is closed with no further effect (except to save any folder selected in project attributes).
Status <static>	Text showing the status of the file, e.g. “Ready to import”, “No valid alarms found”, “That file can't be read”
WorksheetChoice <choice>	Choice box listing all worksheet names in the selected file. When no valid .xlsx file is in PathName, the choice box shows “<None>” and is disabled. If a valid file is in PathName, this lists all worksheets in the order they appear in the file, with the last selection preselected. (The last selection needs to be stored as a project attribute, on a per-alarm file basis.) / When the user chooses a different worksheet in this Choice, several other fields in the Viewport need to be updated.
OverwriteExistingAlarms <checkbox>	If checked, imported alarms will overwrite existing alarms in the project. If unchecked, alarms in the import that match alarm tags in the project will be ignored. / This setting is persistent per project.
HeaderRowCount <spin>	Allows the user to set how many header rows are defined in the worksheet to be imported. These rows will be skipped in the import. Limited to integers 0 ≤ x ≤ 99 (arbitrary limit). This setting is persistent per project.
WorksheetCount <static>	Displays the number of worksheets found in the file named in PathName. Initially blank if pathname is empty or doesn't contain the name of a readable Excel file. Updated whenever PathName changes.
UniqueAlarmCount <static>	Displays the number of unique alarms (total alarms minus duplicates) in the selected worksheet of the file named in PathName. Blank if alarms can't be extracted from the file, including if the alarm or instrument tag field hasn't been selected in any of the the ColXNumber choices.
DuplicateAlarmCount <static>	Displays the number of duplicate alarms (alarms whose alarm tag is the same as another alarm higher up in the selected worksheet). Blank if alarms can't be extracted from the file, including if the alarm or instrument tag column hasn't been specified using the ColXNumber choices.
MultiLevel <checkbox>	In many cases, the alarm spreadsheet for import has one row per instrument tag, with several columns for different alarm levels, e.g. HH, H, L, LL. If the MultiLevel checkbox is checked, Vizop assumes this format, and will parse multiple alarms from each row (for details, see the section on Alarm Parsing in this specification). If unchecked, Vizop assumes exactly one alarm per row.
Import priorities as override <checkbox>	If a column is labelled as containing user alarm priorities: / If this checkbox is checked: / If the column is nonblank: user alarm priorities will be imported, and the alarm's “override priority” flag set to True / If the column is blank: no action taken / In all other cases, no action is taken.
ExampleInstrumentTag <static> and ExampleAlarmTag <text>	When the alarm spreadsheet can be parsed and the user has specified a column containing instrument tag, the first row's instrument tag is is written to AlarmInstrumentTag, followed by “high” (e.g. “LIC-1234 high”). The user must then populate the ExampleAlarmTag with the corresponding hypothetical high alarm tag (e.g. “LAH-1234”. / If MultiLevel is checked, or no column is specified as containing the alarm tag (using the ColXNumber choices), the user must populate this field. A reminder message is written to the Status field when ExampleAlarmTag is required and empty, and cleared when ExampleAlarmTag is populated (including “H” as a minimum). If ExampleAlarmTag is empty when required, the Go button will have no impact.
LeftButton and RightButton <buttons>	Changes which columns of the import file are displayed in the preview. When the file can first be opened, columns 1, 2 and 3 (or the first non-empty columns, if leftmost column(s) are empty) are shown. When RightButton is short left clicked, the displayed columns will change to 2, 3 and 4. On long left click, the columns will change one step, then continue to change repeatedly until mouse button up. LeftButton works similarly in the opposite direction. / Each button are disabled when no more populated columns are available in the specified direction.
ColXNumber <static>	Shows the number of the column currently shown in that slot. Empty when no file can be opened for preview. Updated when the preview is scrolled (using LeftButton or RightButton), the filename is changed, or the worksheet is changed.
ColXAttrib <choice>	Allows the user to select an alarm attribute to import from the column currently in this slot. The choice contains all possible attributes that can be imported. Initially shows “<Do not use>”. Updated at the same times as ColXNumber. Column attribute import selections are persistent per project.
First row preview <static>	Shows cells from the first nonblank row in the selected worksheet. The columns shown are as explained under LeftButton, above.
First/second row after header rows preview <static>	Shows cells from the first and second row of the selected worksheet after the header rows. The header rows are the first N rows (after any blank rows) in the worksheet, where N is determined by the HeaderRowCount field. The columns shown are as explained under LeftButton.
CancelButton <button>	Label: “Cancel”. Destroys the Import alarm Viewport, and returns the previous Viewport to the display device.
GoButton <button>	Executes the import, if all required information is available. Then destroys the Import alarm Viewport, and shows an alarm list viewport on the display device, scrolled to show the first alarm imported. If necessary, a new alarm list Viewport is created. A VizopTalks message is displayed stating the outcome of the import. / The import action is undoable and redoable, and should be saved on the fly.

IMPORTABLE ALARM ATTRIBUTES
The user can specify any or all of the attributes listed below in the ColXAttrib choices, to indicate that they should be imported from the corresponding column of the file. Each attribute can be selected in only one column; once an attribute is assigned to a column, it is not offered in the ColXAttrib choices for any other columns.

Selection of all attributes are optional, except:
- Either the alarm tag must be selected, or the instrument tag plus ExampleAlarmTag widget must contain a text that contains at least a string of digits that is also present in the ExampleInstrumentTag widget (so that Vizop can try to deduce the required alarm tag from the instrument tag).
- Either the Alarm type must be selected, or at least one of the SetpointHH/H/L/LL attributes must be selected.
- If the Setpoint or any of the SetpointHH/H/L/LL attributes is selected, the EngUnit attribute must also be selected (so that Vizop knows what unit to assign to the setpoint value).
- Not more than one of ResponseTimeRequiredInMin and ResponseTimeRequiredCateg attributes may be selected (so that Vizop knows whether to import times as absolute or as category names).
- Not more than one of ResponseTimeAvailableInMin and ResponseTimeAvailableCateg attributes may be selected (so that Vizop knows whether to import times as absolute or as category names).

Column name	Description	Default if not selected
ProcessUnit (str)	Name of process unit in which the alarm is located	blank
InstrTag (str)	Tag of instrument (device) that generates the PV or signal on which the alarm is based.	blank
AlarmTag (str)	Tag of alarm in the Process Control System	Will be populated automatically (see algorithm below)
AlarmType (str; e.g. HH, H, L, LL, high rate of change, discrepancy)	The algorithm used in the PCS to determine whether the alarm is active	H (see algorithm below)
Setpoint (float)	The value of the measured PV at which the alarm becomes active	not set
SetpointHH / SetpointH / SetpointL / SetpointLL (floats)	Used for MultiLevel alarms (see above)	not set
EngUnit (str)	The unit of measure of the setpoint(s) for this tag. Must match a unit that Vizop can recognise.	If blank, the setpoint is set to “not set”
IsDiscrete (bool)	Whether the alarm is a simple on/off alarm (e.g. “door open” alarm).	False
Comment (str)	Free text field for user comments	blank
Cause (list of str delimited by Newline)	Likely causes of the alarm condition	blank
Consequence (list of str delimited by Newline)	Consequences of non-response to the alarm. Each item in this list corresponds to the same position of item in Cause. If Consequence contains exactly 1 item, it will be repeated for each cause. If Consequence contains 1 > N > Causes items, the last Causes-N consequences will be left blank. If Consequences contains more than Causes, the last N-Causes items will be ignored.	blank
Confirmation (str)	How the operator can confirm the alarm is not a false alarm	blank
OperatorAction (list of str delimited by Newline)	Appropriate operator action in response to the alarm. Same algorithm applies as for Consequence.	blank
ResponseTimeRequiredInMin (list of int delimited by Newline)	How much time is needed to execute the operator action. Same algorithm applies as for Consequence.	not set
ResponseTimeAvailableInMin (list of int delimited by Newline)	How much time is available to execute the operator action. Same algorithm applies as for Consequence.	not set
ResponseTimeRequiredCateg (list of str delimited by Newline)	Name of a response time category indicating how much time is needed to execute the operator action. Same algorithm applies as for Consequence.	not set
ResponseTimeAvailableCateg (list of str delimited by Newline)	Name of a response time category indicating how much time is needed to execute the operator action. Same algorithm applies as for Consequence.	not set
Severity (list of str)	Name of a severity category associated with the cause and consequence. Same algorithm applies as for Consequence. Import will be done for each alarm only if all severity categories for that alarm are recognised. If the number of severities provided exceeds the number of causes, excess severities will be ignored. If the number of severities is less than the number of causes, the beginning of the severity list will be filled up, and the remainder left as undefined.	not set
UserPriority (str)	Name of a priority category. Imported only if “override priorities” checkbox is checked (see above)	not set
Classification1~8 (bool)	Whether the alarm belongs to alarm classes 1~8. Classifications are assumed to be in the same order as in the Classifications attribute of the AR object.	False
OnDelay (int)	The on delay of the alarm in seconds	not set
OffDelay (int)	The off delay of the alarm in seconds	not set
PVAveraging (int)	The PV averaging time base of the alarm in seconds	not set
Deadband (float)	The deadband of the alarm	not set
DeadbandUnit (str)	The unit of measure of the deadband. The cell contents should be either % or the same as EngUnit (if EngUnit is selected and populated in this alarm's row). If it is not, or the cell is empty, or this attribute is not assigned to a column, % is assumed (for now; in future, this might be user-selectable).	%

ADDITIONAL ALARM ATTRIBUTES
The following attributes are not imported:

Attribute name	Description	Default if not defined
AutoPriority (category value)	Priority determined from matrix lookup	UndefinedPriority
OverridePriority (bool)	Whether to use UserPriority instead of AutoPriority in the control system	False
Status (category value)	The rationalization status of the alarm (e.g. Not considered, In progress, Action needed, Rationalized, Approved)	Not considered

ALGORITHM FOR DEDUCING ALARM TAG
If the user does not specify a column as Alarm tag, the alarm tag will be deduced from the instrument tag and the ExampleInstrumentTag widget as follows:
Example: ExampleInstrumentTag = “100-FIC-234”, ExampleAlarmTag = “100-FAH-234”
- If ExampleInstrumentTag or ExampleAlarmTag is empty, the import cannot proceed, as Vizop cannot deduce the end of prefix marker.
- Find the instrument tag prefix – the longest string that is present in both ExampleInstrumentTag and ExampleAlarmTag, starting from the left end of ExampleInstrumentTag (after stripping all white spaces from the beginning, middle and end of both strings). Example: “100-F”
- Find the instrument tag prefix end marker – the next character in ExampleInstrumentTag after the instrument tag prefix. Example: “I”. If the whole of the ExampleAlarmTag is in the ExampleInstrumentTag, set the end marker to chr(1), on the assumption this character will never appear in the ExampleInstrumentTag.
- Find the instrument tag suffix – Same as prefix, but starting from the right end of ExampleInstrumentTag after stripping all white spaces, and not allowing any overlap between prefix and suffix. Example: “-234”
- Find the instrument tag suffix start marker – the first character in the instrument tag suffix (or “” if the instrument tag suffix is empty). Example: “-”
- Find the residue in the ExampleAlarmTag between the prefix and suffix. This should contain “H”, which is how the user indicates how to insert the alarm type string; if it doesn't, the import cannot proceed. Get the residue prefix (before the H) and suffix (after the H). Example: residue = “AH”, residue prefix = “A”, residue suffix = “”
- Find the alarm type string. This is “HH”, “H”, “L” or “LL” depending on which of any columns specified as containing SetpointHH / SetpointH / SetpointL / SetpointLL is populated with a string that doesn't contain only white space. (If more than one such column is populated, multiple alarm tags will be created.) If none of these columns is specified (which would be a bug), the alarm type string defaults to “H” (for now; this could be user selectable later). If none of these columns is populated, no alarm will be created for this row.

To generalise this to another tag, the algorithm is:
- Left part of instrument tag up to, but not including, the instrument tag prefix end marker +
- Residue prefix +
- Alarm type string +
- Residue suffix +
- Right part of instrument tag up to and including the instrument tag suffix start marker, or “” if the instrument tag suffix start marker is “”

Example: instrument tag = “200-PDI-500B” would generate alarm tag: “200-PD” + “A” + HH/H/L/LL + “” + “-500B”

IMPORTATION ALGORITHM
1. Starting from the N'th row after the header row (see HeaderRowCount), read one row from the worksheet.
2. The row is importable if:
  - the Alarm tag column is populated with a non-empty string (after stripping all whitespace characters), or
  - an Alarm instrument tag can be deduced (see “Algorithm For Deducing Alarm Tag”)
    and
  - if MultiLevel is True, at least one of the SetpointHH / SetpointH / SetpointL / SetpointLL column is populated with a non-empty string (after stripping all whitespace characters)
1. If the alarm is not importable, skip to step 11.
2. Deduce the alarm instrument tag. If the alarm tag column is populated, use this, otherwise deduce it using the algorithm above.
3. Has this alarm tag already been imported? If so, treat this row as a “duplicate”; skip this row and proceed to the next row.
4. Does this alarm tag already exist in the alarm list, and is OverwriteExistingAlarms False? if so, treat this row as a skipped repeat alarm and proceed to the next row.
5. Parse as many fields as possible from the row (following the rules in the table above).
6. When parsing response time, severity and/or priority category names (as strings), try to match them (non-case sensitive, stripping all white spaces) with existing categories in the project.
7. If response time, severity and/or priority category names (as strings) were read from the file, add to the project any categories not already existing in the project, respecting the limit on the number of categories allowed.
8. If this alarm tag already exists in the alarm list, put the new data into the existing alarm and store the old data in an Undo record. Otherwise, make a new alarm, append it to the alarm list, and put the new data in the new alarm.
9. Increment the row index, go back to step 1 until the last row is reached.
10. If saving on the fly, save the alarm list in the project file.
11. Return statistics from the import (how many rows read, how many unique alarms imported, how many unimportable rows skipped, how many existing alarms overwritten) for display in VizopTalks.