VIZOP: FAULT TREE VIEWPORT SPEC: FULL TREE

Level: 3
Revision: 0.1
Date: 12 Nov 2018

Peter Clarke

OVERVIEW
This document describes one of the Viewports provided in the Fault Tree PHA model: the Full Tree Viewport. It shows the complete fault tree in a display panel.

DETAILS OF VIEWPORT APPEARANCE AND BEHAVIOUR

Standard zoom and pan controls are available; see Control Frame spec for details.

Layout options
Orientation can be Bottom to top (‘Upward’) or left to right (‘Rightward’). Defined as an attribute of the Viewport. Initially we will implement Rightward only.

Display overview
Description below is based on Orientation = ‘Rightward’

The overall display area is divided into 2 stacked areas: header and FT.

Header area
The header area contains overview information, including:
- SIF name (text provided by user)
- Revision number
- Which Risk Receptor (RR) is depicted. If any object in the FT has different values for different RR's, the FT needs to depict only one RR at a time, or a group of RR's for which all the values in the FT are identical. The user can switch between RR's using a choice widget in the header.
- Operating mode (low demand, high demand, continuous)
- Severity value for the FT for the currently displayed RR's, and corresponding tolerable frequency (see notes on tolerable frequency attribute, above)
- Calculated resulting value of the FT
- RRF/PFD/PFH target for SIF
This need not be always visible. It should zoom and pan along with the FT area, and can be panned out of the hosting panel.

FT area
In the FT area, the FT is displayed in “levels” - vertical columns containing all FT objects and Builder buttons (see details below), separated with connecting lines. These columns correspond to the “columns” in the FT data hierarchy (see above).

Any currently selected objects are shown with blue dashed box around them. Objects are selectable according to the standard Control Frame implementation.

Between columns there is a gap containing connecting lines and connect buttons.

Connecting lines: these join outputs and inputs, according to the connectivity specified by the user. The user can disconnect an existing connecting line by double left clicking on it.

Connect buttons: these are shapes shown on the outputs of objects in the column to the left, and on inputs of objects in the column to the right. The functions of the connect buttons are:
- left click on an unconnected output button and drag to an input connect button in the same inter-column gap to make a new connection. (Dragging is constrained within the limits of the inter-column gap.)
- left click on an unconnected input button and drag to an output connect button to make a new connection.
- left click on a connected output or input button and drag off the button to disconnect all connections to that button
- left click on a connected output button and drag to another output button to move all connections from the first output to the second.
- left click on a connected input button and drag to another output button to move its connection from the first input to the second.
If the user makes a connection that “jumps over” an object in the FT (e.g. connects initiating events #1 and #3 to logic gate #1, jumping over initiating event #2), the FT objects are automatically reordered to prevent the need for crossing connections. This reordering is undone if the user uses the “undo” function to undo the connection. However, if the user simply deletes the connection, the reordering is not undone.
Idea for future: builder buttons in the column to the right could also be provided with connect buttons, so that the user can connect to them and create a new object (e.g. logic gate) in one action.

Display of initiating events, IPLs (etc), intermediate events and outcomes:
Each event needs to have a full version and a reduced version. The full version shows:
- Coloured box (colour varies by type of event). If ievent is currently set to “ignore”, everything is greyed out.
- Button to switch to reduced version (affects display in this Viewport only)
- Element type name (initiating event, IPL, enabling condition, conditional modifier, intermediate event, or outcome) in darker coloured bar at the top; with choice box to change from one type to another; and with “ignored” indicator if applicable
- Description (editable TextCtrl)
- Value (frequency, event probability, PFD/PFH, or RRF); user editable if appropriate for this object's Value kind
- Value unit; user editable if appropriate for this object's Value kind
- Value kind (constant, link etc; see class NumValueItem in $$$ implementation spec). User editable if appropriate for this object type
- Whether it is the “SIF failure event” for high demand mode and continuous mode SIFs (applicable only to initiating events) (check box)
- Problem indicator – a symbol like , appears if the value is invalid (if supplied by the user) or cannot be calculated (if it's supposed to be calculated). Clickable to show details of the problem in the control panel (if the Viewport is in the Control Frame). Also consider providing a balloon (box beside the button) that appears while the left mouse button is held down on the button; the balloon gives a summary of the problem.
- Comment buttons (callout symbol) for description and value. Button changes colour to indicate when >0 comments are defined. When defined, comment(s) are listed below the relevant item – the current value of the comment is shown; when clicked, this takes us to the ‘Edit comment’ aspect of the control panel. (TODO: add this to Control Frame spec)
- Action item(s): can be shown or hidden; there’s a single show/hide button (works on all action items at once in this object) and an Edit button (pen icon) per action item, which opens the 'edit action' aspect of the control panel. (Action items that are linked to others are shown with chain symbol in the control panel.). Also an ‘add action item’ button, which opens a new action in the control panel.

The reduced version shows:
- Coloured box (colour varies by type of event) - greyed out if set to “ignored”
- Button to switch to full version (affects display in this Viewport only)
- Description (editable TextCtrl)
- Value (frequency, event probability, PFD/PFH, or RRF); user editable if appropriate for this object's Value kind
- Value unit; user editable if appropriate for this object's Value kind
- Problem indicator – same as full version.
- Comment indicator; visible if any comments are defined. No action on click.
- Action item indicator; visible if any action items are defined. No action on click.

Currently, it is not intended to have a widget inside the object box to indicate whether it is in a collapse group.

Actions on the FT object as a whole:
- Left click on empty space within the object to select/deselect it (following standard selection behaviour for Viewports)
- Left click on empty space within the object, then drag within the column, to reorder objects within the column. Show drag box during dragging. Applies connectivity rules, i.e. only contiguous items can be connected; so if the reordering would break the rule, it's not allowed and has no effect. In this situation, a VizopTalks message will be shown, and ideally the drag box will animate flying back to the original location. Reorder is undoable.
- Right click on empty space within the object to show context menu with commands including Delete, Duplicate, Duplicate and link, commands related to collapse groups, send to event bank (for future version), ignore in calculation/restore to calculation. Commands act on all selected objects.
- Press Delete key to delete all selected objects. Deletion is undoable.
- “Duplicate” command in the PHAModel menu adds a duplicated version of all selected objects in-place. Connections are also duplicated. Attributes in the new objects are marked as “copied from” (see explanation in the $$$ spec).
- “Duplicate and link” command in the PHAModel menu: same as “Duplicate” command, except that the attribute values in the new objects are linked to the originals (see explanation in the $$$ spec).
- Later, we can implement standard copy/paste functions.

Handling of collapse groups:
A collapse group is created by selecting >1 FT object and using the “Make collapse group” command in the context menu and in the PHAModel menu. If the selected objects include a collapsed collapse group, or any objects that are already in a collapse group, the collapse group itself (rather than its contained objects) are included in the newe collapse group. If the selected objects don't meet the rules for forming a collapse group, try to form a collapse group with a similar membership to the selected items (by including/excluding objects) or ignore the command and post a message in VizopTalks. ($$$To do: develop algorithm for this)

A collapse group is modified (add or remove objects from it) by the same procedure as creating one, except that the command is “Update collapse group”. The collapse group will be updated to reflect the currently selected objects. Same principles apply concerning collapse group membership rules.

A collapse group is deleted by using the “Delete collapse group” command in the context menu and in the PHAModel menu. The context command is available in any object that's in a collapse group. The menu command is available when ≥1 of the selected objects is in a collapse group. If any selected object (or the object right-clicked, if no object is selected) are in nested collapse groups, only the “top level” collapse group is deleted, leaving the nested collapse groups intact.

Display of a collapsed group – uncollapsed (i.e. all member objects visible)
Draw a dashed box enclosing all of the members of the group.

Display of a collapsed group – collapsed
Coloured box
Group description (editable TextCtrl)
Combined value (calculated)
Value unit
Problem indicator – if the output value can't be calculated. Clicking on the problem indicator behaves the same as clicking on the problem indicator of the first member of the group that has a value problem, and expands the group.
‘Expand’ button – when clicked, uncollapses the group. This is not undoable, as it's only a display change, not a change to the data set.

Display of a connecting line
Connected objects are shown with a line joining the connect buttons of the objects. The user can disconnect the objects by double clicking on the connect line, as described above.

‘Builder’ buttons
These are buttons displayed above each object in every column, and also at the bottom of the column. The user left clicks them to add a new object at the specified location. There are 2 types of builder button: “new event” and “new gate”. “New event” buttons are provided in odd-numbered columns, and “new gate” buttons in even-numbered columns.

When a new event is created, it is set to the same type as the event above by default, and also added to the collapse group of the event above (if any).
When a new gate is created, it is set to the same type as the gate above by default, if any.

Builder buttons are not FT objects and are not stored in the FT data. They are created “on the fly” for display purposes.

Display of a logic gate:
Gates can be shown in full or reduced display.

Full display:
- Coloured box
- Button to switch to reduced version (affects display in this Viewport only)
- Description (editable TextCtrl)
- Gate type name (e.g. “OR gate”) in darker coloured bar at the top; with choice box to change from one type to another
- Value (output frequency or probability); calculated, not editable
- Value unit
- Problem indicator – a symbol like , appears if the value cannot be calculated (if it's supposed to be calculated). Clickable to show details of the problem in the control panel (if the Viewport is in the Control Frame). Also consider providing a balloon (box beside the button) that appears while the left mouse button is held down on the button; the balloon gives a summary of the problem.
- Comment buttons (callout symbol) for description. Button changes colour to indicate when >0 comments are defined. When defined, comment(s) are listed below the relevant item – the current value of the comment is shown; when clicked, this takes us to the ‘Edit comment’ aspect of the control panel.
- Action item(s): can be shown or hidden; there’s a single show/hide button (works on all action items at once in this object) and an Edit button (pen icon) per action item, which opens the 'edit action' aspect of the control panel. (Action items that are linked to others are shown with chain symbol in the control panel.). Also an ‘add action item’ button, which opens a new action in the control panel.

The reduced version shows:
- Shape depicting logic gate. Logic gate depiction options: see http://de.wikipedia.org/wiki/Logikgatter#Typen_von_Logikgattern_und_Symbolik.
- Button to switch to full version (affects display in this Viewport only)
- Value, value unit and problem indicator if applicable

Context menu (right click on logic gate) offers the following commands:
- Set gate style (see below)
- Copy/cut to clipboard
- Paste from clipboard (if clipboard contains a logic gate, all logic gate settings will be overwritten by the pasted logic gate)
- Duplicate
- Duplicate with link (links description, comments and action items of new gate to the current gate)
- Delete gate

Gates can be included in collapse groups, as described above.

The depiction style of the gates is an overall setting of the project (as we assume it should be consistent across the whole project). Offer IEC 60617-12 (default), ANSI 91, and DIN 40700.
$$$ working here

Display of a connector-in or connector-out:
Connectors in/out can be shown in full or reduced display. Editing of its connections is done in the Control panel. ($$$ to do: define control panel aspect)

Full display:
- Coloured box
- Button to switch to reduced version (affects display in this Viewport only)
- Header showing that it's a connector-in or connector-out
- Long description (editable TextCtrl)
- Short description (editable TextCtrl)
- An indicator “Connected” or “Not connected”
- Value (output frequency or probability); calculated, not editable
- Value unit
- Problem indicator – a symbol like , appears if the value cannot be calculated (if it's supposed to be calculated). Clickable to show details of the problem in the control panel (if the Viewport is in the Control Frame). Also consider providing a balloon (box beside the button) that appears while the left mouse button is held down on the button; the balloon gives a summary of the problem.
- Comment button (callout symbol) for long description. Same behaviour as comment button for other kinds of FT object.
- Action item(s): can be shown or hidden; there’s a single show/hide button (works on all action items at once in this object) and an Edit button (pen icon) per action item, which opens the 'edit action' aspect of the control panel. (Action items that are linked to others are shown with chain symbol in the control panel.). Also an ‘add action item’ button, which opens a new action in the control panel.

The reduced version shows:
- A small box shaped with incoming or outgoing arrowhead
- Button to switch to full version (affects display in this Viewport only)
- Short description (editable TextCtrl)
- Value, value unit and problem indicator if applicable

Control panel aspects

- Edit action items: select action item to edit (might show all action items in Content Window); for selected action item: edit text fields (Responsibility), edit date (a date picker field), link to another action item, whether the action item is in parking lot. For editing the Text of the action item, a special set of widgets is shown (see iWindow mode spec for details). Alco ‘Cancel’ and ‘Finished’ buttons. Clicking anywhere in Content Window treated same as ‘Finished’ button.
- Edit comment: standard Control panel widget set. Shows the widgets for editing of the selected comment (see Control frame spec for details), plus ‘Cancel’ and ‘Finished’ buttons. Clicking anywhere in Control frame treated same as ‘Finished’ button.
- Set up risk matrix (to be defined)
- Analysis (for sensitivity analysis, etc) (future version)
- Connector in/out connections setup (to be defined)
- Numbering (standard numbering management widgets)
- Value linking (to be defined)
- Smart tag numbers (to be defined)

UNDO IMPLEMENTATION
When the user requests Undo or Redo of a change to the FT data set, the undo is executed as follows.

1. The control frame from which the Undo request was sent (call it Control Frame A) calls the undo execution procedure in module undo, which calls the specific undo handler. Undo handlers are in the faulttree module, as methods of class FTObjectInCore, e.g. method ChangeText_Undo().

2. The undo handler performs the data adjustment.

3. The undo handler invokes core procedure UpdateAllViewportsAfterUndo in module controlframe.

4. UpdateAllViewportsAfterUndo needs to force Control Frame A to show the Viewport from which the original change was made, panned to show the field that was undone. To do this:
(a) It fetches full redraw data from the PHA Model, including the coordinates of the relevant field
(b) If the Edit Panel is currently showing a different Viewport, it instructs the Edit Panel to save a milestone (for back navigation) and switch to the Viewport containing the undone field, panned to the required location to show the undone field (at the top left of the panel if it would otherwise be offscreen). Otherwise, it instructs the Edit Panel to re-render the Viewport, panned to the required location.

5. UpdateAllViewportsAfterUndo needs to request updates to all Viewports on other display devices (Control Frames on collaborator machines, and other viewing frames on the “server” machine). For now, just do a complete refresh of all Viewports other than the one on Control Frame A: go through all current Viewport shadows in the datacore, request the respective PHA models to provide full redraw data, and send it to the display devices. No need to adjust pan on the Viewports (unlike step 4) – it would be distracting to the users if the display suddenly jumps.

Eventually, we can optimise this step by sending data only if the Viewport contains the changed item.

UpdateAllViewportsAfterUndo exits and passes control back to the undo handler.

6. The undo handler calls SaveOnFly to save the data change in the recovery file. See specification 3-03 for details.

COMMUNICATIONS WITH CORE

INCOMING MESSAGES

The incoming data string contains, in this order:
- Exactly one FTDisplay definition
- Exactly one FTHeader definition
- Zero or more FTColumn definitions
- Zero or more FTCollapseGroup definitions

FT Display information
<display>
Zoom=(int, 1000x the required zoom value; eg zoom of 0.5 → value of 500)
PanX=(int)
PanY=(int)

FT Header information
<header>
SIFName='XA123' (string)
OpMode='Low-demand' | 'High-demand' | 'Continuous' (string)
Rev='0.1' (string)
RiskReceptors='Safety, Environment' (string)
Severity='Severe' (string)
TolFreqValue='1E-4' (string)
TolFreqUnit='/yr' (string)
OutcomeValue='2.5E-2' (string)
OutcomeUnit='/yr' (string)
TargetUnit='RRF' (string)
TargetValue='40' (string)
BackgColour=0081ff (rrggbb hex digits)
TextColour=12abd8 (rrggbb hex digits)
</header>

FT columns
<column>
ColNo=(int)
[objects]
</column>

FTCollapseGroup information
<collapsegroup>
ID=(int)
CollapsedBool=(int) # 0 = not collapsed, 1 = collapsed (didn't use Bool to make it more future-proof)
</collapsegroup>

Object: generic event (eg cause, IPL, intermediate event)
<event>
ID=(int)
EventType=(str: can be ‘InitEvent’, ‘IPL’, ‘CondModifier’, ‘IntermediateEvent’, ‘TopEvent’)
BackgColour=(rrggbb)
Numbering=(str)
Description=(str: rich text)
Value=(str)
ValueUnit=(str)
Status=int (bitmask: bit 0 = reserved for future, bit 1 = problem, bit 2 = grouped, bit 3 = linked)
CanEditValue = (bool)
DescriptionComment = (str) [can be 0 or more instances]
ValueComment = (str) [can be 0 or more instances]
ValueUnitComment = (str) [can be 0 or more instances]
ValueKindComment = (str) [can be 0 or more instances]
ShowActionItems = (bool)
ActionItem = (str starting with status byte: bit 1 = linked) [can be 0 or more instances]
ConnectTo= (int: ID of object connected to) [can be 0 or more instances]
</event>

Object: logic gate
<gate>
ID=(int)
GateType=(str: can be 'OR', 'MutExcOR', 'AND', 'NOR', 'NAND')
BackgColour=(rrggbb)
Style=(str: can be 'IEC60617-12', 'ANSI91', 'DIN40700')
Numbering=(str)
Description=(str: rich text)
Value=(str: value at gate output)
ValueUnit=(str)
Status=int (bitmask: bit 0 = reserved for future, bit 1 = problem, bit 2 = grouped)
CanEdit = (bool: whether gate can be edited, or is auto-added)
DescriptionComment = (str) [can be 0 or more instances]
ValueComment = (str) [can be 0 or more instances]
ValueUnitComment = (str) [can be 0 or more instances]
</gate>

Object: connector-in
<connector-in>
ID=(int)
BackgColour=(rrggbb)
Description=(str: rich text)
</connector-in>

Object: connector-out
<connector-in>
ID=(int)
BackgColour=(rrggbb)
Description=(str: rich text)
</connector-out>