VIZOP SPECIFICATION
CONTROL FRAME

Level: 2
Version: 0.1 (under initial construction)

OVERVIEW
The Control Frame is the main UI “window” for interaction with Vizop. The user can always see either the Welcome Screen (WS), or the Control Frame (never both).

The main functions of the Control Frame are:
- Provide standard GUI functions such as menus, frame resize, maximise and minimize buttons, scrollbars, tooltips etc.
- Provide user information and prompts through a small panel (VizopTalks panel) that shows messages
- Provide an edit panel for editing the current Viewport
- Provide a control panel for setting parameters of specific objects within the project

The user can also open additional Viewports in separate frames. These can be on the same monitor or a separate monitor. The Control Frame allows the user to control what is shown on each Viewport.

OVERVIEW OF CONTROL FRAME LAYOUT

Standard frame header and menu bar. Currently, no toolbar is planned.
Edit panel, with scrollbars (when required) and zoom tool (when required)
Control panel	VizopTalks panel
View panel: Space for controlling which open project is visible, and for controlling multiple frames (other frames can also show Viewports)

Currently, no status bar (typically shown at the bottom of the frame) is planned, as it is not an effective way to communicate with the user.

EDIT PANEL
The edit panel shows whichever Viewport is currently selected by the user, using functions in the View panel. The edit panel will always show a Viewport – it will never be empty.

Where appropriate, the Edit Panel should implement the following functions for Viewports. Edit Panel UI behaviour should be standardised as much as possible, for consistent behaviour between types of Viewport and PHA model. Consider that additional Viewport and PHA model types are likely to be added in future.

Function	Meaning	Notes
Zoom	Magnification of the information displayed	When appropriate, the Control Panel shows a zoom tool, which looks like a knob with a pointer showing the currently applied zoom factor. The zoom tool should be shown in a standardised location: bottom centre of the Edit Panel. / The zoom tool offers the following functions: / Left click on zoom tool and drag: dragging upwards or rightwards increases the zoom. Draggining downwards or leftwards decreases the zoom. Zooming is centred on the currently selected object in the Viewport, if it is visible, otherwise the centre of the visible portion of the Viewport. The display should respond to the drag in real time (i.e. not wait for the mousebutton up). / Double left click on zoom tool: if currently zoomed, zoom is reset to 100%. Otherwise, restore the last zoom level. Thus repeated double clicks effectively toggle between zoomed and not zoomed.
Pan	Offset of the display image in the edit panel	Left click and drag on an empty space in the edit panel to pan. The display should respond to the drag in real time (i.e. not wait for the mousebutton up). / Double left click on an empty space in the edit panel: if currently panned (i.e. not the start/origin of the image is not at the top left of the edit panel), reset the pan to zero. Otherwise, restore the previous pan. Thus repeated double clicks effectively toggle between panned and not panned.
Select object(s)	Select one or more object(s) in the Viewport	Here “object” means an entity forming part of the Viewport, such as an event in a Fault Tree. / Left click on an object (without dragging) to select it and deselect all other objects. / Shift + left click on an object to select it and all other objects between it and the nearest (or most recently) selected object / Ctrl (PC) / Command (Mac) + left click on an object to select it without deselecting others. If the object was already selected, deselect it (i.e. toggle select). If the mouse is dragged with Ctrl/Command held down, the toggle is applied to all objects within the rectangle enclosed by the drag start and end points.
Cut, copy, paste
Focus	Move focus from one object to another	Press Tab / Shift + Tab to move the focus from one object to another. Generally, if an object is focused, it means that object (and only that object) is selected.
Delete	Delete an object	Press Delete (or Backspace key on PC) to delete focused object or selected object(s).
Undo, redo	Undo, redo last edit operation	Press Ctrl + Z (PC) or Command + Z (Mac) to undo the last edit operation on the current Viewport. The undone operation should be made evident, where possible, by panning to the applicable object(s), selecting them, and highlighting the edit. / Redo function: similar. Keyboard shortcut TBC.
Edit functions	Provide edit functions specific to the object	Right click (or Menu key on PC) to activate a context menu containing edit functions appropriate to the object(s) selected.
Text edit	Edit text in the object	Allow standard text editing functions in TextCtrl widgets

NOTES ON ZOOM AND PAN

Viewports can be zoomed and panned. The position and size of PHA objects in each model are stored in ‘canvas coordinates’, which are independent of zoom and pan. Utility functions are available to convert these to and from screen coordinates.

Zoom and PanX/Y are attributes of the Viewport, not the Edit panel. The rationale is that they should not belong to panels, because if a Viewport is moved to a panel on another display device with different physical size, the same zoom/pan should apply. They should not belong to PHA models, because one PHA model could be simultaneously viewed in multiple Viewports with different zoom/pan.

To take account of differing physical size of display devices, each display device will have attributes as follows:
- DispScaleFactor (float): factor to multiply zoom by, so that the display model looks similarly proportioned on each display device. Based on constant StandardDispDeviceSize in module controlframe.
- DispOffsetX/Y (int): pixel offset so that display model appears in the same relative location in each display device (ie not crammed into the top left corner of a higher-resolution screen).

Definitions
Zoom (int): % magnification of the display. 100% is “normal size”, in which a distance of 1 canvas unit corresponds to 1 pixel. If Zoom = 200, 1 canvas unit = 2 pixels. Zoom is assumed to be always the same in X and Y axes. Integer value is used to avoid having to do int(round(Zoom)) for display of Zoom values.

PanX, PanY (int): offset of the drawing origin, in pixels. If (PanX, PanY) = (10, 20), canvas coord (0, 0) should be drawn at panel coordinates (10, 20). Zoom is applied before Pan when calculating canvas coords (in other words, the Pan offset is not zoomed):
ScreenX = DispOffsetX + PanX + (DispScaleFactor * Zoom/100 * CanvasX)
where ScreenX is the X-coord to draw at, relative to the origin of the drawing panel, and CanvasX is the X-coord of the logical object being drawn, as it is internally calculated (with no zoom or pan).

CONTROL PANEL
The Control Panel provides widgets allowing editing of attributes. It offers “aspects” (pages of attributes) selectable by tabs (or other means, TBC). The aspect currently displayed aims to “follow” the current user action as appropriate; for example, if the user selects an object in the current Viewport, the aspect flips to show editing attributes relating to the selected object.

Aspects offered by the Control Panel are listed below.

Aspect name	Content	When available
Viewports	Open and close viewports, and move them around in available display frames	When the current project has any PHA models that can display Viewports in the Edit Panel. / Available viewports relate to currently existing PHAModels, the project, document lists, and global settings such as keyboard shortcuts and colour schemes.
PHAModels	Open and close PHA models	Always. When a new project is opened with no PHAModels, this aspect is shown by default.
Search	Interact with user during a text search	When the current project has any Viewports open in any display frame
Project	(anything?)
Numbering	Set up object numbering	When a numberable object is selected in the current Viewport
Tags	Set up smart tag numbers in the current text field	When a text field is selected in the current object in the Viewport
Constants	Set up constants in the project	Always
Numerical value	Adjust properties of a numerical value

Implementation:
- Aspects are instances of class ControlPanelAspectItem
- Switch to new aspect: GotoControlPanelAspect
WIDGETS THAT ARE ALWAYS VISIBLE
Some widgets will be visible in all aspects as follows:

Widget name	Action	Notes
Navigation buttons	Move selection forward or back in history in Edit Panel	The CF needs to keep a history list of which Viewport is shown in the Edit Panel, and which objects are selected in the Viewport, to enable navigation. See Navigation History section in Control Frame implementation spec for details.
Undo, redo buttons	Execute undo/redo of edit actions	Refer to Undo/Redo specification in another document

GUI BEHAVIOURS
The following functions should be set up in the Control Panel where feasible, and with as much standardisation as possible between aspects:
- Keyboard shortcuts (based on Ctrl (PC) / Command (Mac) modifier)
- Tooltips
- Tab traversal, in a logical sequence
- Text field contents to be saved automatically when the TextCtrl loses focus
- Changes to data fields are reflected immediately in the project data set, i.e. Viewports are updated immediately, without needing to press an “Apply”/”OK” button
- Pre-population of widgets: fields should be pre-populated back to the last used settings where appropriate. For example, in the Search aspect, options should be retained from the previous search. For switch fields such as “Case sensitive search”, we may consider offering options including No, Only this time, and Always. If the user chooses Only this time, the option reverts to No next time.

ASPECT: “NUMERICAL VALUE”
GUI layout:
[label] Value: [value name] in [hosting element] [1]				[button] comment [2]
[label] Current value	[textbox] value [3]	[choice] unit [4]	[label] Basis	[choice] ValueKind [5]
[label] Linked to [n] other value(s) [6]		[show this label only if the value is linked to any other values]
[Only one of the rows below is visible, depending on ValueKind]
[if ValueKind is Linked]	[button] Link from… [7]	[button] Show me [8]
[if ValueKind is Copied]	[button] Copy from… [9]	[button] Show me [10]
[if ValueKind is Constant]	[label] Constant:	[choice] constants [11]	[button] Edit constants [12]
[if ValueKind is Lookup]	[label] Matrix:	[choice] matrices [13]	[button] Edit matrices [13]

Notes:
[1] Header label: displays component name and element name; e.g. “Value: Tolerable frequency in FT header”
[2] Comment button: jumps to Comment aspect of control panel. When Comment aspect finishes with “Done” button, return to the Numerical Value aspect.
[3] Value: display current numerical value. If the ValueKind is User or Copied, the value is editable; otherwise, it is read-only. If ValueKind is Linked, and if the link source is undefined, Value shows “<Link undefined>”.
If the user edits the value, call the handler that attempts to write the new value back into the component. If the new value is accepted, perform the same routine as if the value was edited in place (i.e. write it back correctly, store it in the component, store an undo record, perform save on the fly, etc.)
[4] Unit: choice box containing human names of all permissible units for this value. Preselected to the current unit. Editable if the ValueKind is User or Copied; if edited, follow the same as [3].
[5] ValueKind: choice box containing human names of all permissible ValueKinds for this value. Preselected to the current ValueKind. If edited, follow the “change of ValueKind” algorithm.
[6] “Linked to n other value(s)”: display this static text only if the value is linked to other values; show the number of values linked to. (For future, we may add a “show me” button to show the values linked to.)
[7] “Link from” button: When clicked, VizopTalks displays “Navigate to the value to link from, and click “Link””. The VizopTalks panel shows a “Link” button and a “Cancel” button. The user can now navigate to anywhere in the project and click on a numerical value; the Control Panel will behave as it normally would during navigation; all editing operations and most menu commands are blocked. The user needs to click “Link” to make the link (see “Make link” algorithm) and return all panels to their state when the “Link from” button was clicked. Alternatively, the user can click “Cancel”, same action as “Link” except the link is not made.
[8] “Show me”: When clicked, Vizop navigates to the component that the value is linked from. All panels are updated. (The user can get back to the previous display using the “back” button.) If the link source is not defined, the “Show me” button is disabled.
[9] “Copy from” button: similar to “Link from” button [9], for ValueKind “Copied”.
[10] “Show me” button: similar to [8].
[11] “Constants” choice box: lists the human names of all constants defined in the project, with the currently defined constant for this value preselected. If the value has no constant selected, a special option “<Select a constant>” is selected. If there are no constants in the project, “<No constants defined>” is selected. If the user selects an option, and if the option is a constant, the selected constant is assigned to this value; see “Select constant” algorithm.
[12] “Edit constants” button: when clicked, the control panel goes to the “Edit constants” aspect, preselected with the constant currently selected in [11], if any. The “Edit constants” aspect will include a “Use this constant” exit button, which returns to the “Numerical value” aspect and assigns the currently edited constant to the value.

IMPLEMENTATION [TODO: move this to level 3 or 4 spec]
Initial creation of Control panel aspects:
During __init__ of Control panel: call MakePHAModelsAspect, then SetInitialEditPanelAspect
MakePHAModelsAspect: does actions specific to this aspect
- creates the aspect and its widgets
- calls PHAModelsAspect.Initialize
PHAModelsAspect.Initialize: does setup actions general for all aspects
- creates the notebook tab for the aspect and puts it in the notebook
- makes an empty sizer for the aspect
SetInitialControlPanelAspect: requests display of the initial aspect
- If the project has any PHA models: (to do)
- Else: calls GotoControlPanelAspect to request the PHAModels aspect

To change to a different aspect, call GotoControlPanelAspect
GotoControlPanelAspect:
- Calls Deactivate() method of previous aspect, if any
- Calls Prefill() method of new aspect, which puts required values into widgets
- Calls Activate() method of new aspect
- Adds new aspect to notebook (if not already in notebook)
- Switches notebook to show new aspect

Activate:
Calls ActivateWidgetsInPanel for widget list of the requested aspect

ActivateWidgetsInPanel:
- Binds event handlers for widgets
- Registers keyboard shortcuts for widgets

Deactivate:
Calls DeactivateWidgetsInPanel for widget list of the requested aspect

DeactivateWidgetsInPanel:
- Unbinds event handlers for widgets
- Deregisters keyboard shortcuts for widgets

VIEW PANEL
This is a space for controlling which open project is visible, and for controlling multiple frames (other frames can also show Viewports).

PANEL LAYOUT
The layout of this panel depends on whether multiple projects are open. If only one project is open, the whole panel is available for Viewport selection buttons.
If >1 project is open, the panel is divided into 2 areas, side by side:
- Left side: a switch to select whether the View panel shows projects, or Viewports within the current project. The default position of this switch is:
  - Same as the last position selected by the user
  - Switched to “projects” if the user has just opened >1 project in one go (from command line or open project request from WS or CF menus)
- Right side: Project selection buttons, or Viewport selection buttons, depending on the seeting of the switch in the left side

VIEWPORT SELECTION BUTTONS
One button is provided for every existing Viewport in the project. The buttons are arranged in a row. If there are too many buttons for the panel, a scrollbar is provided.

Each Viewport selection button is a vertical stack of 2 buttons:
Viewport name
Name of frame where Viewport is visible

The Viewport name is a human-readable name such as “Node list” or “Alarm rationalization: LAH-123”. This name needs to be supplied by the Viewport object.
The Frame name is blank if the Viewport is not currently shown on any open frame. If the Viewport is shown, the frame name will be something like “Window 2 on here” (meaning: a “slave” frame on the same monitor as the CF) or “Projector” (meaning: a slave frame on another display device).

The functions of the Viewport selection buttons are:

Action	Name of function	Details
Short left click on Viewport name	Open on CF	The Viewport is displayed in the CF's Edit Panel. The Viewport previously displayed in the Edit Panel is no longer visible.
Long left click on Viewport name, without dragging beyond the limits of the button	Preview on CF	The Viewport is temporarily displayed in the CF's Edit Panel, as long as the left mouse button is held down. The Viewport previously displayed in the Edit Panel is temporarily not visible. / During this time, editing of the Viewport is blocked. However, zoom and pan might be possible if the user is using a multitouch display. / When the left mouse button is released, the Edit Panel reverts to the previous Viewport.
Left click and drag on Viewport name	Move Viewport to device	Dragging is considered to start when the mouse pointer moves outside the limits of the starting button. / During the drag, a box (same size as the Viewport button) is displayed under the mouse pointer, as a visual confirmation that dragging is occurring. / Dragging is confined to within the View panel area. If the user drags to the left or right edges of the View panel, the panel will scroll to the left or right to show any Viewports that are scrolled off the screen. / If the user drops the drag on another Viewport button or non-blank Frame name button, the Viewport is displayed on that frame. The Viewport previously shown on that frame is no longer visible. The frame previously showing that Viewport still shows the same Viewport (because we are not allowing a frame to be empty).
Right click on Viewport name	Viewport context menu	Opens a context menu with options: Delete Viewport (other options to add?)
Short left click on Frame name	Select frame	Opens a context menu showing all available frames, plus a “New frame” option for the master display device (the device hosting the CF), plus “New frame on X” options for any other attached display devices (e.g. X = “projector”). The user can then left click on one of the options, or press Esc (or click outside the context menu) to close it. / When an option in the context menu is clicked, the Viewport associated with the Frame named on the button is also shown on the selected device. If the selected device is a new frame, a new Viewport + Frame button is created for it, immediately to the right of the Frame button that was clicked.
Long left click on Frame name	Preview associated Viewport on CF	Same as “Preview Viewport on CF”, above. / Works even if the Frame name button is blank (i.e. the Viewport is not currently shown in any frame).
Right click on Frame name	Frame context menu	Opens a context menu with options: Delete frame (not offered if the Frame is the CF). In future, options might include showing the frame on collaborators' CF.

VIZOPTALKS PANEL
The VizopTalks panel is a message panel to allow Vizop to communicate with the user. It is intended to provide helpful, non-intrusive, context-sensitive, timely user guidance, and to minimise the need for pop-up dialogues. Its main intended functions are:
- Provide confirmation
- Provide warnings
- Show prompts
- Show tips
- Ask the user questions

The VizopTalks panel can show:
- A heading (larger/bolder font)
- Short text messages
- A small number of response buttons
- A coloured background

The background colour is changed automatically among the following:
- A neutral colour for messages requiring no user response
- A stronger colour for prompts
- A yet stronger colour for warnings

Apart from tips, messages can be defined to remain visible for a minimum period of time (say 10 seconds) to allow the user time to read them. Tips can remain visible for a time defined by flowschemes shown below.
- If the tip is context specific, it remains visible as long as that context is applicable. After that, it will be removed.
- If the tip is not context specific, it remains visible for a fixed period (say 10 seconds). After that, it is removed, to make way for the next message in the queue (or blank panel, if there's no queued messages).
- If a higher priority type of message is queued while the tip is displayed, the tip will be immediately replaced by the new message.

Messages can be submitted to VizopTalks by any object, including the project itself, a PHA model, a Viewport, and an action (e.g. search) in the CF.

Message priorities are defined as follows.
Implementation: class instances of class VizopTalksPriority

Name	Background colour	Description
Lowest	Neutral	For blank messages
Status	Neutral	For unimportant status updates
Tip_general	Neutral	For user tips (optional features that the user can ignore) relating to general features of Vizop
Tip_context_general	Neutral	For user tips specific to the part of Vizop the user is using, e.g. Fault Tree, HAZOP node list.
Tip_context_specific	Neutral	For user tips specific to the precise task the user is doing, e.g. “right click to see more options”
Confirmation	Neutral	To confirm that an action (e.g. opening a project) was completed successfully
Instruction	Moderate	For user guidance that, if ignored, may make it difficult or impossible for the user to execute certain functions. Example: user entered an invalid value. No MinLife set.
Caution	Moderate	Information to the user that doesn't require immediate action, but could cause difficulties if not addressed later. Has a MinLife set.
Option	Moderate	Information needed from the user – non-critical (i.e. Vizop can proceed without a response)
Warning	Intense	Information to the user that affects the quality of work, e.g. problem with parsing data from a project file
Question	Intense	Information needed from the user – critical (i.e. Vizop cannot proceed without a response)
Critical	Intense	Inform the user of a problem that may lead to data loss, e.g. bug found

Implementation details
Tips are stored in lists: one for Tip_general and one for Tip_context_general. When a tip is to be shown, a tip is selected randomly from the available tips in the list, and marked as “Shown” so that tips will not be repeated unnecessarily. Tip_general tips are never repeated within one instance of Vizop. Tip_context_general tips will not be repeated while the applicable context is still active, but the “Shown” flag is reset when the context changes, so the tip can be re-displayed next time the context is active.

The VizopTalks panel has 2 timers: MinLife timer, which is running when a message is displayed for its guaranteed minimum lifetime; and Timeout timer, which is running when the displayed message should be removed after a certain time.

The VizopTalks panel has 4 callable methods: 1. Submit incoming message (including tips), 2. Expiry of the MinLife timer, 3. Expiry of the Timeout timer, 4. Change of user working context. These methods handle all required code to implement the required algorithms.

Flowschemes for each method
Method 1: When incoming message is submitted to VizopTalks for display
Implementation: procedure SubmitVizopTalksMessage

1. Is the incoming message a Tip_general or Tip_context_general? If yes, and if it's not already there, store it in the applicable tip list, mark it as “unshown” and (for Tip_context_general list only) mark it as “relevant to the current context”.
2. Is there any existing (currently displayed) message?
No: go to step 10
3. Is the MinLife timer running?
Yes: Put the new message in the message buffer and exit.
4. Is the Timeout timer running?
No: go to step 10
5. Is the priority of the incoming message higher than that of the existing message?
Yes: stop the Timeout timer and go to step 10
No: Put the new message in the message buffer and exit
10. Display the incoming message and (if applicable, depending on its priority) start the Minlife and Timeout timers. If it's a tip, mark it as shown in the tip list. Exit.

Method 2: On MinLife timer expiry
Implementation: procedure OnMinLifeTimer
1. Is there any message in the message buffer?
Yes: go to step 2
No: go to step 10
2. Is the buffered message priority higher than the existing message?
Yes: go to step 20
3. Is the Timeout timer running?
Yes: do nothing (wait for Timeout timer expiry). Exit.
No: go to step 20
10. Is the Timeout timer running?
Yes: do nothing (wait for Timeout timer expiry). Exit.
11. Are there any unshown, relevant messages in the Tip_Context_General tip list?
Yes: Show the next Tip_Context_General message (chosen randomly from all unshown messages in the list), mark the message as shown, and start timers as appropriate to the definition of the Tip_Context_General priority (above). Exit.
12. Are there any unshown messages in the Tip_General tip list?
Yes: Show the next Tip_General message (chosen randomly from all unshown messages in the list), mark the message as shown, and start timers as appropriate to the definition of the Tip_General priority (above). Exit.
No: Leave the current message on display and exit.
20. Display the buffered message, clear the buffer, stop the Timeout timer if running, and start timers according to the definition of the buffered message's priority. Exit.

Method 3: On Timeout timer expiry
Implementation: procedure OnTimeoutTimer
1. Is there any message in the message buffer?
Yes: display the buffered message, clear the buffer, and start timers according to the definition of the buffered message's priority. Exit.
2. Are there any unshown, relevant messages in the Tip_Context_General tip list?
Yes: Show the next Tip_Context_General message (chosen randomly from all unshown messages in the list), mark the message as shown, and start timers as appropriate to the definition of the Tip_Context_General priority (above). Exit.
3. Are there any unshown messages in the Tip_General tip list?
Yes: Show the next Tip_General message (chosen randomly from all unshown messages in the list), mark the message as shown, and start timers as appropriate to the definition of the Tip_General priority (above). Exit.
No: clear the currently displayed message, leaving VizopTalks blank. Exit.

Method 4: On change of user context
Implementation: procedure ChangeUserContext
1. Mark all tips in the Tip_Context_General tip list as “not relevant to the current context.” (Don't delete them – we need to retain their “shown” status for when the user returns to the previous context.)
2. Delete all tips in Tip_Context_Specific tip list. (The context can reinstate them next time, and they can be repeated.)
3. Is the existing message a Tip_Context_General or Tip_Context_Specific? If no, exit.
4. Cancel the Timeout and Minlife timers, if running.
5. Go to Method 3.

OVERALL CONTROL FRAME FUNCTIONS
This section describes features of the Control Frame as a whole.

User action	Function	Notes
Close control frame (click “X”/red button)	Treat as a request to close all open projects, thus reverting to the WS	All Slave frames would be closed as well
Resize control frame	The control frame is maximised by default. It can be full screen. It can be used in split screen mode (MacOS). It can be maximised and minimised (usual GUI functions, clicking buttons in title bar / double-clicking header etc.). It can be resized (drag frame edges/corners).	Control frame is constrained to a defined minimum size determined by the following: / The Control panel, View panel and VizopTalks panel are all fixed height / The Control panel and View panel have a minimum width (enough to allow their controls to be operated meaningfully) / The VizopTalks panel is fixed width / The Edit panel has a minimum height, so that it can't disappear completely
Move control frame within the same display device	Control frame can be moved (usual GUI function: drag title bar)
Move control frame to another display device	Control frame can be dragged to another display device (usual GUI function)	All Slave frames remain on the same device they are currently on / The “primary display device” is redefined as the device the control frame now resides on.

CONTROL FRAME MENUS
This section describes menus provided in the Control Frame menu bar.
At present, it is assumed the lineup of menus will be the same at all times. However, the list of commands within each menu can be varied according to the operating need at the time.

Menu name	Commands	Notes
File	Open project / Save project (available when project is not set to save on fly) / Close project / Close all open projects (available when >1 project open) / (divider) / Menu items relating to import and export / (divider) / About Vizop / Quit Vizop
Edit	Undo / Redo / (divider) / Project settings / (divider) / Preferences
Tools	Menu items relating to: / collaboration / multiple monitors
PHAModel	Create PHA Model Delete PHA Model / (divider) / PHA model specific menu items, e.g. add node, add SIF
Report	Menu items for creating reports

SLAVE FRAMES
Each instance of Vizop, when ≥1 project is open, has 1 Control Frame and ≥0 Slave frames. A Slave frame is a window showing only a Viewport (plus standard frame tools such as maximise and minimise buttons and a Close button).

When a project is opened, Vizop will restore the same lineup of Slave frames when the project was saved. However, any Slave frames that were previously on devices that don't seem to exist (e.g. projector not plugged in) will not be restored. For each restored Slave frame, the following attributes will be restored:
- Viewport currently shown in the frame
- Zoom and pan
- Frame position and size on the device (however, Vizop will check that the position and size make sense given the current resolution of the device, in case it has changed, and adjust accordingly)
- Whether the frame was minimised
- Whether the frame was on top
- The order of Viewports and frames shown in the View panel (including any Viewports that were on frames that can't be restored, but showing their frames as blank)

New Slave frames can be created by left clicking on a Frame name button in the View panel. When a new Slave frame is created, it will be maximised in the device and placed on top. (Later, we might add a function to set the size according to other frames in the device. For example, if the user seems to have resized a frame to the left half of the device, the new frame can be sized to fill the remaining space on the right.)

Slave frames can be destroyed by:
- Using the Delete frame function in the Right click context menu of the Frame name button in the View panel
- Clicking the “X” button of the frame itself
When a Slave frame is destroyed, the View panel is updated accordingly. Also, any other Slave frame on the same device is brought to the front. If the destroyed Slave frame had focus, focus switches to the Control Frame.

Slave frame creation and destruction is undoable and redoable.

LAUNCH
When launched, the CF first checks if the current project has any PHA models. If it does not have any, the CF invites the user to create one by the following steps:
- Prompt message in VizopTalks
- Set Edit panel to New-PHAModel aspect
Implementation: module controlframe, procedure InviteUserToCreatePHAModel

KEYBOARD SHORTCUTS
Keyboard shortcuts will be available for as many functions as possible in the Control frame. The defined keyboard shortcut will be made known to the user in the usage context where feasible, either directly (e.g. on a button label) or in a tooltip.

General principles:
- Follow typical shortcuts (common for other apps)
- Use intuitive keystrokes and key combinations
- Avoid shortcuts that, if easily mistyped, could have major undesired consequences
- Eventually, we may allow the user to remap keyboard shortcuts. However, this is not a “must have” and we don't have to consider it in early code versions.

Global keyboard shortcuts
The following keystrokes will be consistently available in all applicable usage conditions in the Control frame.
In the table below, Mac keyboard modifier keys are shown. For Windows, substitute Command → Control, Option → Alt.

Keystroke	Meaning
Command + Z	Undo
Command + Y	Redo
Command + C, V, X	Copy, paste, cut
Command + left arrow	Navigate backwards
Command + right arrow	Navigate forwards

Implementation
Keystrokes are registered in RegisterKeyPressHandler, a global list in module ControlFrame.
Setting up keystroke detection and handling: RegisterKeyPressHandler in module vizop_misc
Removing keystrokes from register: UnregisterKeyPressHandler in module vizop_misc
Detecting keystrokes: OnIdle

TOOLTIPS
Tooltips are pop-up help balloons that appear when the mouse hovers over a specified area on the screen. They will be available for as many widgets as possible in the Control frame.

Implementation: Currently using the basic wx.ToolTip. We tried wx.adv.CustomToolTip (check name) but it didn't seem to work well with panels in the advanced layout manager. We can also try SuperToolTip.