VIZOP SPEC: HAZOP PHA MODEL

OVERVIEW
The PHA model supports the recording of qualitative and semi-quantitative PHA studies including HAZOP, CHAZOP, What-If and Checklist.

DISPLAY MODELS: SUMMARY
Name	Purpose	Belongs to what kind of parent object	Accessible to read-only members of the project?	Status (in this document)
Process Unit list [not just 'Unit', to distinguish from numerical value units]	Display and edit a list of the process units	project	Yes	Drafted
Node list	Display and edit a list of the nodes in one specific process unit	process unit	Yes	Drafted
Risk matrix	Set up and edit one of the risk matrices in the project, used for risk ranking	project	Yes	Drafted
PHA setup	Display and edit PHA setup information, including deviations to apply to all nodes	PHA object	Yes	Drafted
Node worksheet	Display and edit a traditional grid-style PHA worksheet for one node	node	Yes	Drafted
Cause worksheet	Detailed view of one cause including alarm rationalization parameters	cause	Yes	Drafted
Alarm list [remove from PHA spec to alarm handling spec?]	Set up and edit list of all process alarms in unit	process unit	Yes	Not started
Recommendations list [remove from PHA spec?]	List view of all recommendations in the unit	process unit	Yes	Not started. Not specific to HAZOP display model
PHA worksheet report	Full worksheet in report format read only	PHA object	No	Started (working here)
Node list report		PHA object	No
Unit list report		PHA object	No
Recommendations report [remove from PHA spec?]		project	No	Not started. Not specific to PHA display model
Clickable P&ID	P&ID annotated to show summary of cases studied. Clickable to enter new data	P&ID	Yes	Not started
P&ID list	List of P&IDs in the process unit	Process unit	Yes	Not started

DISPLAY MODEL: PHA setup
This is the entry point for a new, empty PHA object.
An editor user is able to define the following properties, which are attributes of the PHA object:
- Terminology to be used: define singular and plural terms for: deviation, node, cause, consequence, safeguard, likelihood, severity, recommendation, unit, P&ID, alarm, risk matrix, type of PHA being performed (eg HAZOP or What-If)
- Types of node available, eg tank, reactor, header, batch process, sequence. This will be pre-populated with a few options from the company profile (a profile containing settings that are consistent for all users within an organisation).
- Default deviations for each type of node. (This is to provide similar functionality to PHAx's “smart deviations.”) For example: No flow, More flow, Composition change, Utility failure. Pre-populated from company profile.
- The type of node applied to the current PHA object. It's one of the list of types of node available. When a project is opened, if a PHA model in the project contains a type of node not found in the current list, the incoming type of node will be added to the list, but not stored in the config.
- Subset of all project P&IDs that are included in this PHA. (P&IDs are defined at project level.) This could be a check list box of all P&IDs.
- Whether the PHA object allows active P&ID view. (Some types of PHA may not use P&IDs or be amenable to interactive working on P&IDs.) By default, it's allowed.

A read-only user can view the current settings of all the above, but cannot change any of them.

DISPLAY MODEL: UNIT LIST
The user can see and edit the list of process units defined in the current project. Functions provided:
- Listbox showing currently defined units, including the default unit
- 'Add unit' button
- 'Delete unit' button (however, can't delete the last remaining unit; there must be at least one unit in the project)
- 'Rename to' textbox (when user navigates away from it, unit is renamed)
- Fields to edit unit properties: Comment (text), whether to include in report (Boolean: defaults to True), whether to include in this PHA (Boolean: defaults to True), (any other properties)
A read-only user can view the list of units, but cannot perform any of the functions above.

DISPLAY MODEL: NODE LIST
The user can see and edit the list of nodes defined in each process unit in the current project. Functions provided:
- Choice box showing currently defined units – selects a unit to work with
- Listbox showing currently defined nodes in the selected unit
- 'Add node' button
- 'Delete node' button
- 'Duplicate node' button (new copy is inserted immediately below existing node) (all attributes of the copy, and of all its children objects, are marked as 'copied from' the existing node. Later, we could offer an option to link the new node's attributes instead of copying)
- 'Rename to' textbox (when user navigates away from it (including to 'Done' button), node is renamed)
- Buttons for 'move to top', 'move to bottom', 'move up' (1 position in node list) and 'move down'
- 'Transfer node to' function: select another unit in a choice box, hit 'Transfer' button (it will be transferred to the end of the node list in the other unit)
- 'Import from another project' function (future)
- Fields to edit node properties: (comments are applicable to each; provide comment buttons)
  - whether to include in report (Boolean: defaults to True)
  - whether to include in this PHA (Boolean: defaults to True)
  - numbering (use standard number defining system)
  - design intent (multiline text)
  - description (multiline text)
  - operating parameters (multiline text)
  - (any other properties)
A read-only user can view the list of units, but cannot perform any of the functions above.

DISPLAY MODEL: RISK MATRIX
Allows the user to see what risk matrices are defined in the project, and edit them.
Functions provided:
- Choice box showing currently defined risk matrices – selects a risk matrix to work with
- Import a risk matrix from another project (button) (future)
- Add / delete / duplicate matrix (buttons)
- Fields to edit risk matrix properties:
  - human name (text)
  - how many dimensions: 1, 2 or 3 (choice)
  - name of dimension 1 (eg “Frequency”) (text)
  - name of dimensions 2 and 3, if applicable (2 x texts)
  - name of values in the matrix (eg “Risk level”)
- Listbox of values in dimension 1 (eg “Rare”, “Occasional”, “Frequent”). User selects a value to work with, in the listbox. Fields are available for the following attributes and functions:
  - Add (at the bottom of the list) (button)
  - Delete (button) (however, you can't delete if there's only 1 value in the list)
  - Duplicate (button)
  - Rename (text)
  - Reverse (button) (reverses the order of all values in the dimension)
  - Set descriptor (an optional longer text giving detailed meaning of the value, eg “Expected to occur once in the lifetime of the plant”)
  - Set abbreviation (text) (could be a letter, number, short form or whatever the user chooses)
  - Set background colour for display (colour swatch button, using platform's standard colour picker). (The foreground colour will be black or white as necessary to contrast with the background colour.)
  - Functions applicable to the dimension as a whole:
    - Use For (what kind of object can select values in this dimension): check list box offering Cause, Consequence etc [or maybe better to do this in the definition of the object itself]
- Similar for other dimensions and for matrix values
- Matrix layout diagrams. This consists of one or more matrices, showing the dimension values prefilled, and with dropdown boxes in each value slot for the user to pick a matrix value. For 1-D matrices, the box has just 2 columns: dimension values, and matrix values. For 2-D matrices, the box has D1+1 rows (D1 is the number of items in dimension 1) and D2+1 columns. For 3-D matrices, there are D3 boxes, each (D1+1 x D2+1) in size, and with the value of a D3 item shown above it.
- 'Done' and 'Cancel' buttons

DISPLAY MODEL: SINGLE CAUSE VIEW
In PHA, a Cause will be the basic object storing the analysis, not a Deviation. This is to allow a cause to be associated with multiple deviations.
This view shows a single cause in detail and allows a simple LOPA to be done. It also allows setting of alarm parameters needed for AR.
It allows conditions to be defined, which affect the consequence (for example, startup/normal operation, or small/large leak). To use conditions, the user sets the “Apply conditions” checkbox. Then the other condition-related fields appear. Initially the condition list contains 1 item, “All conditions”.
Node: (title)	Node name (choice) (allows jumping to another node)	Button: go to node overview	Button: go to P&ID view	Main deviation: (title)	Main deviation to which cause belongs (choice)
Cause (multi-line free text)		Cause frequency (choice from matrix)		'See also' deviations: (title)	other deviations to which this cause belongs (check list box, excluding main deviation)
Apply conditions (checkbox)	Currently defined conditions (listbox with current selection highlighted)	Probability (title)	Probability (textbox; can contain % to denote percentage) (highlighted yellow if they don't add up to 1.0)	Name (textbox)	Rename (button) – renames currently selected condition	Add (button) – adds condition with name provided in Name textbox
Divider
Consequences (title and total count of consequences)	Consequence titles (listbox) (untitled consequences: use first part of text)	Icon buttons: add tagged element, add conseq, delete conseq, copy/link all from another cause, move up/down, copy in/out, link in/out		Finished (checkbox) (user can query which conseqs are unfinished)
Name: Conseq title (text)	Conseq text (multiline text)	Severity (title)	Risk receptor name (static text) / [1 row per RR]	Severity for risk receptors (choice from matrix) / [1 row per RR]
Divider
Safeguards (title and total safeguard count)	Safeguard titles (listbox) (untitled safeguards: use first part of text)	Icon buttons: add tagged element, add safeguard, delete safeguard, move up/down, copy in/out, link in/out
Safeguard (multiline text)	Icon buttons: add tagged element, add safeguard, delete safeguard, copy/link all from another consequence, move up/down, copy in/out, link in/out	PFD/RRF (title. Works out automatically whether it’s PFD or RRF from value in value box)	PFD/RRF (value box)	Icon button: calculate (calculates required PFD/RRF to meet tol freq. This would be used for SIFs)	Is alarm (checkbox; auto-check if “alarm” element associated with this safeguard) / Is SIF (checkbox)
	Residual conseq if safeguard works: (title)	Residual conseq (multiline textbox)	Severity of residual conseq: (title)	Severity per RR (same structure as original severity)	Note: This row is only needed if SG is alarm or SIF
If safeguard is an alarm:	Best alarm for this case (checkbox)	Operator response: (title)	Operator response (multiline text)	Time avail to respond: (title)	Time avail (choice from matrix)
	May need dynamic suppression (checkbox)	Rationalize now (button, jumps to alarm view)
Divider
Residual frequency (title)	Tolerable frequency (title)	Residual risk (title)	Risk from risk matrix, per RR
Resid freq (static text, calcd)	Tol freq (static text, calcd from matrix)
Recommendations/ parking lot/ doc fixes (choice, determines which type is shown to the right)	Current recommendation/ etc (multiline text)	Icon buttons: add tagged element, add recom/etc, delete recom, show next/previous, copy in/out, link in/out	Details (button) (recom. View, allows editing of fields such as time limit, who by)

DISPLAY MODEL: PHA REPORT
This is an Excel report showing the full worksheet for all nodes. It is in an N-column format of fixed width, designed for direct copy/paste into a Word document in landscape format. (N is a fixed number, not yet determined.)
In the following, fixed text is in bold. Fixed texts marked [S] are skipped if the associated field is empty; others are shown, and the field is populated with “<not defined>”. All empty cells in each row should be merged with the cell to the left.
Comments are inserted above the next divider. If there are any comments, the structure is as follows, with the comments listed in 2 columns – half consecutively in the first column, the remainder in the second column.

Comments
[comment # in square brackets]	Comment text	(empty)	[comment # in square brackets]	Comment text			(empty)

PHA REPORT STRUCTURE
<PHA model type, eg HAZOP> worksheet
Unit	Unit name			Comment[S]	Unit comment			Node count:	# of nodes
<divider>
Node	Node number	Node name			Design intent[S]	Design intent
Description[S]	Description				Operating parameters[S]	Operating parameters
<divider>
Deviation	Deviation name				No causes identified (if deviation is empty)
Cause[S] Cause 1 with numbering	Consequence[S] Consequence 1 with numbering (if no conditions )			Severity[S] / RR1 name: RR1 severity / RR2 name: / RR2 severity etc	Safeguards (skip heading if no safeguards and user didn't opt to include “no safeguards” text)
Likelihood likelihood value, if defined					Safeguard 1 with number, or No safeguards identified if user opted to show this text		PFD = PFD or RRF = RRF [S]	Residual consequence: residual consequence [S]
Condition condition 1 (condition%), if defined	Consequences start here if conditions defined				<Checkbox> Best alarm if safeguard is an alarm and is designated as best alarm for this consequence	Operator response: operator response, if defined and if safeguard is an alarm		Time to respond: time to respond, if defined and if safeguard is an alarm	$$$
	Residual frequency if defined	Residual frequency, if defined	Tolerable frequency if defined	Tolerable frequency, if defined	Safeguard 2 with number... etc
	Residual risk if defined	Residual risk, if defined			Recommendations if any defined for this consequence	Recommendation 1 with number		Responsible: responsible party if defined	(add any other recom. fields such as time limit, whether doc fix)
					Recommendation 2 with number... etc
	Consequence Consequence 2... etc
Condition condition 2 (condition%)... etc
divider
Deviation	Next deviation...etc
End of node node number
divider
Node	start of next node... etc
divider
Unit	start of next unit... etc

NAVIGATION BETWEEN DISPLAY MODELS
As far as possible, navigation between display models should be standardised across all PHA models. (Navigation to other non-PHA models needs to be defined.) To include:
- Forward and back buttons
- Means to copy or send current model to another display device (meaning, another screen on the same computer, or to another project member's screen)
- Jump to “recently used” display models (number of “recent” models to be defined in user's profile)
- Jump to any other PHA display model. For models with multiple instances (eg node worksheet; there's one worksheet for each node), a sub-list allows the user to choose which instance to jump to.
- Exit to Edit Centre.

NOTES
Need to handle deviations and cases that don’t naturally fit into the Deviation – Cause – Consequence – Safeguards pattern. Example: maintainability. Consider having Deviation – Issue – Safeguards pattern, or a customisable pattern.