VIZOP SPECIFICATION
PROJECT FILE (XML) SPECIFICATION

30 Jan 2019
Version: 1.0
Peter Clarke

INTRODUCTION
This document describes the details of the format used for saving project data in a file.
The project file uses XML. The XML structure is shown in the table below. The structure doesn't show end tags (</Tag>) for clarity.
Tags will nearly always contain the object's ID number as their contained text. The reason for doing this (instead of including ID as an attribute of the tag) is: (1) the tag needs to contain some text, otherwise the parser sometimes gets confused, and every object will have an ID; (2) ID is probably the only piece of data that every object will have, so it's consistent to use ID as the content.

The following symbols are used in the table (not in the actual XML):
·       * indicates tags that contain values only, not other tags. (The * should not appear in the actual file.)
·       % indicates tags that can be repeated. (If non-% tags are repeated, only the first instance in each level will be used.) (The % should not appear in the actual file.)
·       B indicates tags that can contain <Bookmark> tags. (The B should not appear in the actual file.) The structure of a <Bookmark> tag is as follows:
         <Bookmark>*% BookmarkSerialNumber
</Bookmark>
Bookmark serial numbers are in the order the bookmarks were created.
·       C indicates tags that can contain <Comment> child tags. (The C should not appear in the actual file.) The structure of a <Comment> tag is as follows:
         <Comment>%B CommentSerialNumber
</Comment>
·       N indicates tags that contain numerical values. The value (real or integer) must come immediately after the tag, and before any child tags. The tag can optionally contain the following child tags:
o   a <Unit> tag, whose value is the engineering unit of the numerical value. Valid values are: None, Prob (indicating probability), %, /yr, /hr, FIT, hr, day, wk, month, yr. All are non-case sensitive. If the <Unit> tag is absent, a default unit is taken (varies per parameter).
o   a <Kind> tag, whose value indicates the kind of the number. Valid values are: Manual (value entered by user), Constant (value fixed to a defined constant), Calc (value calculated according to a formula), Lookup (value looked up in a 2D matrix), Category (one of a list of values defined separately), Linked (value fixed to that of another parameter) (all are non-case sensitive). Defaults to Manual. Currently only Manual is implemented, and other kinds will give undefined results.
- U indicates tags that can take an attribute “Status” (for use by Save On The Fly). For example, <Node Status=Deleted>. The Status attribute is optional. Recognised values are detailed in the “Project open and save” specification. Unrecognised values of Status will be ignored (normally silently; a message can be output if we are in Verbose mode).
- ! indicates compulsory tags. If missing from the file, vizop can't open the project. All tags not marked ! can be omitted.
Element IDs are unique for all elements (including comments) across entire project.
Leading and trailing whitespace (spaces, tabs and newlines) in text values are removed on reading and writing the XML file.
Boolean tag values are written as True or False. When reading the file, any of the following is considered as True: True, Yes, Y, 1 (not case-sensitive). Any other value is considered as False. If the Boolean value is to be defined as “unset”, the tag should be omitted.
In general, we will avoid too deep embedding of object tags inside other objects, to minimise the amount of data needing to be written by Save On The Fly.

OVERALL FILE STRUCTURE
<VizopProject VizopVersion=[VersionNumber]
Project information tags (e.g. project name, description, team members, edit number)
Structured object tags (process units, risk receptors, numbering systems, risk matrix, constants)
PHA object tags (e.g. FT, alarm rationalization); see details below
Comment tags
Action item tags
Update tags – these are added during Save On Fly. During project file opening, they will be present only if this is a recovery project file, i.e. Vizop did not terminate properly. They are defined in the Save On Fly specification.
</VizopProject>

DETAILED STRUCTURE OF EACH KIND OF TAG
PROJECT INFORMATION TAGS
<ShortTitle [text] />
<ProjNumber [text] />
<Description [text] />
<EditNumber [int as text] />
<TeamMembers> sequence of TeamMember tags </TeamMembers>

TEAMMEMBER TAGS
One tag per team member defined in the project. There shall be ≥0 <TeamMember> tags in the file.
<TeamMember> <ID [ID int as str] /> <Name [Name as str] /> <Role [Role as str] /> <Affiliation [Affiliation as str] /> </TeamMember>

PROCESS UNIT TAGS
One tag per section of process equipment in the project. There shall be ≥0 <ProcessUnit> tags in the file.
<ProcessUnit> <ID [ID int as str] /> <UnitNumber [UnitNumber as str] /> <ShortName [ShortName as str] /> <LongName [LongName as str] />
</ProcessUnit>

RISK RECEPTOR TAGS
One tag per risk receptor (safety, environment etc.) used in the project. There shall be ≥0 <RiskReceptor> tags in the file.
<RiskReceptor> <ID [ID int as str] /> <Name [HumanName as str] /> </RiskReceptor>

NUMBERING SYSTEM TAGS
One instance of each unique numbering system is defined. As many PHA objects will have the same numbering system, we don't want to repeat the numbering system unnecessarily. There shall be ≥0 <NumberingSystem> tags in the file.
<NumberingSystem> <ID [ID int as str] />
then ≥1 of: <Chunk> <Type ['str', 'Parent' or 'Serial'] /> [other fields according to Type] </Chunk>
Other fields:
Type str: <Value> [text content of string field] </Value>
Type Parent: <ID [ID of parent object from which numbering is obtained] />
Type Serial:	<Fieldwidth [field width, int as str] />
<PadChar [pad character, single character as str; needs to be escaped if not a printable character, e.g. %20 for space] />
<StartAt [initial value in sequence, int as str] /> [can be omitted if 1]
<SkipTo [value to skip to, int as str] /> [omitted if None]
<GapBefore [how many numbers to leave before this item, int as str] /> [can be omitted if 0]
<Include [IncludeInNumbering attrib, bool as str] /> [can be omitted if True]
<NoValue> [NoValue str] </NoValue> [always included, even if IncludeInNumbering is True, as we should keep any value set by the user]

RISK MATRIX TAGS – storing the contents of a LookupTableItem. There shall be ≥0 <RiskMatrix> tags in the file.
<RiskMatrix>
Define ≥1 categories, e.g. “severity high”, which are instances of CategoryNameItem:
<Category> <ID [category ID as str] /> <Name> [HumanName of dimension, e.g. 'Severity'] </Name> <Description> [description str] </Description>
</Category>
<SeverityDimension [SeverityDimensionIndex int as str] />
Define ≥1 dimensions:
<Dimension> <Name> [HumanName of dimension, e.g. 'Severity'] </Name>
Define ≥1 keys in the dimension: <Key> <ID [ID of category key as defined just above] /> </Key>
</Dimension>
Define entries (values) per dimension, per key, in this order:
Dimension 0 key 0, dimension 1 key 0…
Dimension 0 key 0, dimension 1 key 1… etc until all dimension 1 keys used up
Dimension 0 key 1, dimension 1 key 0… etc
<Entry> [value, see below for XML structure of values] </Entry>
</RiskMatrix>

CONSTANT TAGS
One tag per constant defined in the project. There shall be ≥0 <Constant> tags in the file.
<Constant> <ID [ID int as str] /> <Name [HumanName as str] />
<LinkFrom [ID of linked-from constant as str] /> [omitted if this constant does not get its value by linking from another constant]
<ConstValue> [value, see below for XML structure of values] </ConstValue> [omitted if this constant is linked from another constant]
[If the constant is linked from another constant, and the linked-from constant's ID is missing in the project file, this constant's value is set to an appropriate NumProblemValue, allowing Vizop to inform the user that the linked-from constant is missing.]
</Constant>

COMMENT TAGS
One tag per unique comment defined in the project. There shall be ≥0 <Comment> tags in the file.
<Comment> <ID [ID int as str] /> <Text> [text of comment as str, suitably escaped] </Text>
</Comment>

ACTION ITEM TAGS
One tag per unique action item defined in the project. There shall be ≥0 <Action> tags in the file.
<Action> <ID [ID int as str] /> <Text> [text of action as str, suitably escaped] </Text> <Responsible> [responsible party's name, str] </Responsible>
<Deadline> [deadline date, str] </Deadline>
</Action>

VALUES
Values are embedded inside other tags. They define how a number (e.g. frequency of an initiating event) is set in the project – for example, the number could be fixed by the user, linked to another value, or looked up from a risk matrix. They are stored in XML as follows:
< [tag name according to the attribute being stored, e.g. “Frequency” ]>
<Kind [kind of value: 'User', 'Constant', 'Lookup', 'Category', 'Copied', or 'Link'] />
Other tags according to Kind:
Kind = User:
For each risk receptor defined for this value:
<RiskReceptor> <ID [risk receptor ID, str] /> <Value> [value as str] </Value> <Unit [ID of engineering unit] />
<Infinite [whether infinite, bool as str] > [omitted if not infinite] </RiskReceptor>
Kind = Constant: <ID [ID of constant, str] />
Kind = Lookup: <ID [ID of lookup table, str] />
Define a lookup value for each dimension of the lookup table: <Value> [value to look up in this dimension] </Value>
(We store actual lookup values, rather than index of values in the matrix, so that the lookup will still be correct if the user adds to or deletes some keys from the matrix)
Kind = Category: <TableID [ID of lookup table, str] /> <DimensionID [ID of dimension in lookup table, str] >
For each risk receptor defined in the project:
<RiskReceptor> <ID [risk receptor ID, str] /> <Value> [value to use from this dimension] </Value> </RiskReceptor>
Kind = 'Copied': (this represents a ParentNumValueItem instance)
For each risk receptor defined for this value:
<RiskReceptor> <ID [risk receptor ID, str] /> <Value> [value as str] </Value> <Unit [ID of engineering unit] />
<Infinite [whether infinite, bool as str] > [omitted if not infinite] </RiskReceptor>
<CopiedFrom [ID of value this value was copied from. It is not guaranteed that an existing value with the matching ID still exists; if it does not exist, when the project file is loaded, this value should be converted to kind = User] />
Kind = Link: (this represents a UseParentValueItem instance) <ID [ID of PHA object to which this value is linked, str] />
</ [tag name]>

Outermost tag: <vizopProject>
<ProcessUnit>%BU	ID (int)
	<PHA>*%	ID of a PHA object belonging to this process unit (int)
<RecommendationReport>BU	(show report properties)
<RiskMatrix>%BU	ID (int)
<FaultTree>%BU	ID (int)			Attribs: / GateStyle= (style of logic gates used throughout this FT) / OpMode= (SIF operating mode)
	Header data C	Tags containing data such as SIF number . (This isn't handled as an attrib as it may contain spaces)
	<Column>*% ColumnID	ID of a column in this Fault Tree. Columns are listed in order from left to right (or bottom to top, for vertical display).
<FTColumn>%BU	ID (int)	Tag containing details of a column in a Fault Tree.
	Header data	Any data referring to the column as a whole, such as horizontal/vertical offset
	Tags for FT elements *%BC	See separate table below for details of FT element tags. Tags are listed in order from top to bottom.
<PHA>%BU	ID (int)
	<Node>*%	ID of a node belonging to this PHA (int)
<Node>%BU	ID (int)
	<Cause>*%	ID of a cause object belonging to this node (int)
<Cause>%BU	ID (int)
<Alarm>%U	ID (int)
<Comment>%U	ID of comment (int)
	<Text>*	Text of comment (ignored if Link is supplied) (text)
	<CopiedTo>*%	ID of a comment this comment has been copied to (int)
	<Link>*	ID of a comment to which this comment is linked (i.e. this comment is the 'shadow' of the other comment) (int)

FT ELEMENT TAGS

<FTEvent> %BC	Tag detailing an event such as an initiating event, IPL, intermediate event, final event, conditional modifier or enabling event.		Attribs: / Kind= / Description= / ConnectTo= comma-separated list of objects this event is connected to (on the right of this object) / IsSIFFailureEvent= bool (optional; default is False) / IsFinalEvent= bool
	Optional child tags: / <Value> C: user-defined value of the event / <ActionItem> %C: ID of action item attached to this event / <CollapseGroup> %: ID of collapse group to which this event belongs / <ViewMode>: contains attribs for each user-switchable viewing feature, e.g. CommentsVisible (whether comments are visible), ActionItemsVisible
<FTGate> %BC	Tag detailing a logic gate		Attribs: / Kind= OR, AND etc. / Description= / ConnectTo= comma-separated list of objects this gate is connected to (on the right of this gate) / Gate style not included here as it is assumed to be consistent across the whole FT.
	Optional child tags: / <ActionItem> %C: ID of action item attached to this gate / <CollapseGroup> %: ID of collapse group to which this gate belongs / <ViewMode>: contains attribs for each user-switchable viewing feature, e.g. CommentsVisible (whether comments are visible), ActionItemsVisible, Expanded (all details visible, rather than only gate symbol)
<FTConnector> %BC			Attribs: / Kind= in or out / Description= / ConnectTo= For connector-in, IDs of elements connected (to the right of this connector); for connector-out, IDs of connectors-in attached to this connector (could be empty list).
	Optional child tags: / <Value> C: if value is user-defined (because it's a connector-in feeding a value from a different project), the value is supplied here / <ActionItem> %C: ID of action item attached to this connector / <CollapseGroup> %: ID of collapse group to which this connector belongs / <ViewMode>: contains attribs for each user-switchable viewing feature, e.g. CommentsVisible (whether comments are visible), ActionItemsVisible